Date: July 05, 2006

Student Name:  Andres Riffo

TAs:  Adam Barnett

Otto Goethals

Instructors:   A. Antonio Arroyo

Eric M. Schwartz

University of Florida

Department of Electrical Engineering

EEL 5666 Intelligent Machine Design Laboratory

Weekly Report 7 (05 July 2006)

Okay progress both last and this week. I believe that I am caught up with the schedule of the class. Unfortunately, due to some misunderstandings in the requirements for this week, my written material may seem sub par.  Also, due to family affairs, I will be losing the better half of this week and will not be able to build on CHUMIA. However, I feel in a very strong position and clearly understand my next moves. Next week I will be going at this project hard and I will be producing good results.

Summary of project:

Platform:

Assembled and built. Half of required sensors attached. Saving the rest for precise attachment in order to maximize space and efficiency (small area to mount). Drive servos attached. Arm and Scoop mechanism being assembled. Collision avoidance achieved.

Actuation:

All hacked servos working well. Problem with the same kind of servos having different result of PWM signal. Timers working well.(This took me most of break week.)

Sensors:

Analog IR Sensors working perfectly. Digital sensors worked in simulation but are having a hard time in avoidance. Going to try to attach them to ADC pins. CMUCAM working fine and able to pick up target color (blue – green). Need to build UART for CAM/board interface (will be time consuming). Bump sensors fine and need to build resistor pack for them. The Solar Panel I’ve been testing needs to be replaced from local store.

Code:

Got a handle on timers and interrupts during the break and can effectively use them.

A06645