Date: 	6/7/2007

Student:	Chad J. Fralick

TA:	Adam Barnett

Kevin Claycomb

Instructors:	Dr. A. Antonio Arroyo

Dr. Eric M. Schwartz

Robot:	WaterBot

University of Florida

Department of Electrical and Computer Engineering

EEL 5666

Intelligent Machines Design Laboratory

Weekly Report 4

This week, I ordered several parts for WaterBot and currently await delivery:

- Sonar modules SRF05 from www.acroname.com (obstacle avoidance)

- IR line-following sensors OPB745 from www.digikey.com (finding plants)

- Comparators LM339 from www.digikey.com (IR line-following circuit component)

- LEDs for visual status indicators from www.digikey.com

- Motor driver chips (free) LMD18200 from www.national.com (I ordered these before I learned that boards may be provided)

I also purchased or acquired some parts for WaterBot:

- Tubing for water delivery from Wal-Mart

- 6” Diameter rubber wheels from Wal-Mart

- Keypad from old telephone for possible data input device

I built a cable to connect my LCD to the controller.  I copied code from imdl.freeforums.org (courtesy of Adam Barnett), installed it on the controller, and got the LCD working.

I researched more on RFID and decided to use a different type of sensor/design to distinguish between one plant and another.  I made this decision based on cost, ease of use and installation, and the physical limits of RFID.  I have designed a new method for identifying plants on a path using magnetic actuated switches.  I already have the switches necessary for WaterBot to distinguish up to 32 different plants; realistically, the WaterBot design for this class will accommodate up to 8 different plants (an infinite number of indistinct plants). Each plant will only need a few magnets to distinguish it from any other plant.

During this next week I plan to work on the drive train design, measure the drive motor stall current, order a water pump, and start designing/acquiring a water level sensor.