Technical Data Sheet 3/1/2004                                                                                                                                                          By: Dean Morrison

MIPS2000

mips2000.gdf

Description:

- The MIPS2000 processor executes the assembly program loaded into its Program Memory

• Inputs: 	1 (Clk)

Schematic Symbol:

Machine Instruction Formats:

MIPS2000 Instruction Set:

MIPS2000 Opcode Matrix:

| Opcode | x0 | x1 | x2 | x3 | x4 | x5 | x6 | x7 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  | x8 | x9 | xA | xB | xC | xD | xE | xF |
| 00 | R-Type Instr | bgez | j | jal | beq | bne | - | - |
|  | addi | addiu | slti | sltiu | andi | ori | xori | lui |
| 10 | - | - | - | - | - | - | - | - |
|  | - | - | - | - | - | - | - | - |
| 20 | lb | lh | lwl | lw(r) | lbu | lhu | - | - |
|  | sb | sh | swl | sw | - | - | swr | - |

R-Type Instruction Function Matrix:

| Function | x0 | x1 | x2 | x3 | x4 | x5 | x6 | x7 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  | x8 | x9 | xA | xB | xC | xD | xE | xF |
| 00 | sll | - | srl | sra | sllv | - | srlv | srav |
|  | jr | jalr | - | - | - | - | - | - |
| 10 | mfhi | mthi | mflo | mtlo | - | - | - | - |
|  | mult | multu | div | divu | - | - | - | - |
| 20 | add | addu | sub | subu | and | or | xor | nor |
|  | - | - | slt | sltu | - | - | - | - |

Available Address Modes:

Register-to-Register:

The opcode for all Register-to-Register addressing mode instructions is 0x00, and the

instructions are differentiated by their function.  The two source registers encoded in the

instruction word (Rs and Rt) are operated on according to the function also encoded in the

instruction word, and then the result is placed into the specified destination register Rd.

Immediate:

In Immediate addressing mode, the data for the first operand is contained in the one source

register Rs encoded in the instruction word and the second operand is given as

immediate data, also encoded in the last 16 bits of the instruction word.  The destination register

for I-type instruction is then the Rt register.

# Footnotes

See the R-Type Instruction Function Matrix for the R-Type Instructions

# Text boxes

Pipeline Architecture: