A Multi-Channel Temperature Measurement System with Wireless Data Transmission

Summa Cum Laude Thesis

Dean R. Morrison

Bachelor of Science in Computer Engineering

Spring 2005

Table of Contents

Index of Tables	4

Index of Figures	5

Project Abstract	6

Introduction	6

Technical Objectives	6

Concept Screening Matrix	7

System Level Presentation	9

System Diagrams	9

Subassembly Diagrams	10

Software	16

Temperature Capture Assembly (TCA)	16

RF Repeater	18

PC Interface Assembly	19

USB Data Capture	20

PC Graphical User Interface	21

Testing and Verification	23

Temperature Capture Assembly	24

RF Repeater	24

PC Interface Assembly	24

PC GUI	25

Complete System	25

Final Product	26

Performance	26

Cost Estimation	27

Study Organization	29

References and Acknowledgements	30

APPENDIX I: Bill of Materials	32

APPENDIX II: Source Code	34

1.	TCA: TCA_software.c	34

2.	TCA: TCA_wireless_protocol.h	48

3.	TCA, RFR, PCIA: kilnTemp_defs.h	50

4.	RFR: RFR_software.c	52

5.	RFR: RFR_wireless_protocol.h	58

6.	PCIA: PCIA_software.c	60

7.	USB: PCIA_main.c	67

8.	USB: USB_LE_host.h	77

# Index of Tables

Table 1: Requirements specifications	7

Table 2.0: Concept Screening Matrix – Definition of Concept Variables	7

Table 2.1: Concept Screening Matrix – Concepts A through E	8

Table 2.2: Concept Screening Matrix – Concepts F through J	8

Table 2.3: Concept Screening Matrix – Concepts K, L, Reference	8

Table 3: Differences between chosen concept and final product	9

Table 4: System specifications	26

Table 5: Prototype Cost	28

Table 6: Preliminary Task Schedule	29

Table 7: Final Task Schedule	30

Table 8: References and acknowledgements	30

Table 9.0: TCA bill of materials	32

Table 9.1: RFR bill of materials	33

Table 9.2: PCIA bill of materials	33

# Index of Figures

Figure 1: Overall System Visualization	9

Figure 2: Assembly Interactions	10

Figure 3: TCA Block Diagram	11

Figure 4: TCA Circuit Diagram	12

Figure 5: RFR Block Diagram	13

Figure 6: RFR Circuit Diagram	14

Figure 7: PCIA Block Diagram	15

Figure 8: PCIA Circuit Diagram	16

Figure 9: TCA Microcontroller Software Flowchart	17

Figure 10: RFR Microcontroller Software Flowchart	18

Figure 11: PCIA Microcontroller Software Flowchart	19

Figure 12: USB Data Capture Software Execution	20

Figure 13.0: PC GUI – Tabular Data View	21

Figure 13.1: PC GUI – Graphical Data View	22

Figure 13.2: PC GUI – Calibration Sheet	22

Figure 14: Packet structure	24

Figure 15: Preliminary Gantt Chart	29

Figure 15: Final Gantt Chart	30

# Project Abstract

The goal of this project was to design and build a multi-channel temperature measurement system with wireless data transmission. This system is intended to be used for various industrial process-monitoring applications with a particular focus on the cement and ceramics industries. There are three basic components to this system: (1) a low-power temperature acquisition module, (2) an array of RF repeater modules, and (3) a PC interface module. The data acquisition module will travel with or near the target industrial product, taking several temperature samples at different locations. This data is processed and sent wirelessly to the array of RF receivers. These receivers then forward the data to the PC interface module which, in turn, transmits the data to the PC. A graphical user interface allows the user to monitor the various temperature channels in real time. The system is reconfigurable for a variety of industrial environments and temperature ranges.

The challenge of this project is to compensate for the accumulation of measurement error through the various stages of data transmission. Amplification, analog-to-digital conversion, and signal transmission can all introduce errors in the measurement data, and the total error must be minimized and corrected.

The final outcome of this project is a fully-functional temperature acquisition system that meets and surpasses customer specifications. The versatility of this system is exemplified by its reconfigurable hardware and software components.

# Introduction

The primary application of this product is for process-monitoring in the cement and ceramics industries. Secondary applications include virtually any type of industrial process-monitoring where real-time temperature data is desired and where wireless data transmission is necessary.

Most of the existing products in the cement and ceramics industries do not employ telemetry and therefore are either not real-time or are constrained in their range by cables. Making temperature measurement real-time in these industries will significantly increase productivity and reduce overhead. The combination of data logging with real-time measurements will help the industries recognize and predict trends in their process-monitoring and will aid in increasing efficiency.

# Technical Objectives

The requirements specifications for this design are presented in Table 1 on the following page.

Table 1: Requirements specifications

| Requirement number | Parameter | Conditions | Value | Unit |
| --- | --- | --- | --- | --- |
|  |  |  | Min | Nominal | Max |  |
| 1 | Detectable temperature | B-type | RT |  | 1820 | Celsius |
|  |  | C-type | RT |  | 2320 | Celsius |
|  |  | J-type | RT |  | 1200 | Celsius |
|  |  | K-type | RT |  | 1372 | Celsius |
|  |  | R-type | RT |  | 1768 | Celsius |
|  |  | S-type | RT |  | 1768 | Celsius |
|  |  | T-type | RT |  | 400 | Celsius |
| 2 | Transmission period |  | 0 | 60 | 180 | seconds per packet |
| 3 | Transmit-side supply voltage | Rechargeable batteries | 2.4 |  | 4.8 | Volts |
| 4 | Transmit-side power consumption | Max load |  |  | 0.1 | Watts |
| 5 | Transmission frequency |  | 2.4 | 2.4 | 2.524 | GHz |
| 6 | Wireless transmission range |  |  | 10 | 20 | meters |
| 7 | Temperature resolution |  |  | 2 | 5 | Celsius |
| 8 | Electronics box width |  |  |  | 18 | cm |
| 9 | Electronics box height |  |  |  | 18 | cm |
| 10 | Electronics box length |  |  |  | 18 | cm |
| 11 | Ambient temperature inside electronics box |  |  |  | 200 | Celsius |
| 12 | Duration in kiln |  | 45 |  | 540 | minutes |

# Concept Screening Matrix

The matrix used to select the design concepts that were pursued during this project are shown below in Tables 2.0 – 2.3.

Table 2.0: Concept Screening Matrix – Definition of concept variables

Table 2.1: Concept Screening Matrix – Concepts A through E

Table 2.2: Concept Screening Matrix – Concepts F through J

Table 2.3: Concept Screening Matrix – Concepts K, L, Reference

As the tables above show, Concept C ranked the highest among all of the proposed concepts. Throughout the development of this system, several modifications were made to Concept C in order to increase functionality and to better comply with the requirements. Table 3 outlines the differences between Concept C and the final product.

Table 3: Differences between chosen concept and final product

| Variable | Concept C | Final Product | Justification for change |
| --- | --- | --- | --- |
| Voltage source | Four rechargeable D-size batteries | Four rechargeable AA-size batteries | Four AA batteries can provide the desired current and are significantly smaller than four D batteries. |
| Analog-to-digital conversion | Multi-channel | Single-channel | The multi-channel A-to-D implementation requires more hardware than the single-channel, and the latter implementation will still meet timing requirements. |
| Thermocouple type | R-type | B-, C-, J-, K-, R-, S-, and T-type | The benefits of designing for various thermocouple types outweighs the costs in added hardware. |

# System Level Presentation

### System Diagrams

The product designed is shown below (Figure 1) in a visualization of its operating environment.

Figure 1: Overall system visualization

This system is made up of three assemblies: the Temperature Capture Assembly (TCA), the RF Repeater (RFR) array, and the PC Interface Assembly (PCIA). The functional relationships between these assemblies are depicted in Figure 2.

Figure 2: Assembly interactions

### Subassembly Diagrams

The Temperature Capture Assembly (TCA) shown in Figure 2 has an internal functional structure that is depicted in Figure 3. Figure 4 shows the corresponding circuit diagram for the TCA. The main purpose of the TCA is to sample analog voltages that represent temperature readings from the 16 thermocouples attached to it. These voltages are amplified, digitized, and transmitted wirelessly via the onboard 2.4GHz transceiver. Among the data transmitted by the TCA is the ambient temperature inside the heat-shielding box where the TCA is housed. This temperature is measured by the microcontroller’s integrated temperature sensor. The TCA is powered by a 4.8V rechargeable battery source.

Figure 3: TCA Block Diagram

Figure 4: TCA Circuit Diagram

The RF Repeater (RFR) shown in Figure 2 has an internal functional structure that is depicted in Figure 5. Figure 6 shows the corresponding circuit diagram for the RFR. The main purpose of the RFR is to receive the temperature data that is wirelessly transmitted by the TCA and forward it to the PC Interface via an RS-485 serial interface. By utilizing RS-485 line drivers, the distance between each RFR and the PCIA can be up to 4000 ft. Each of the eight RFRs are powered by the PC Interface’s unregulated power supply, which is between 5V and 9V DC.

Figure 5: RFR Block Diagram

Figure 6: RFR Circuit Diagram

The PC Interface Assembly shown in Figure 2 has an internal functional structure that is depicted in Figure 7. Figure 8 shows the corresponding circuit diagram for the PCIA. The main function of the PCIA is to communicate between the array of up to eight RFRs via an RS-485 serial interface and to receive the temperature data that is transmitted by these RFRs. The PCIA then transmits the real-time temperature data to a data logger (PC, Laptop, etc.) via a USB interface. The PCIA is powered by a single 5V – 9V source that will be regulated to 3.3V.

Figure 7: PCIA Block Diagram

Figure 8: PCIA Circuit Diagram

### Software

#### Temperature Capture Assembly (TCA)

The MSP430F149 Microcontroller on the TCA executes the C-code shown in Listing 1 of Appendix II (associated header files are shown in Listings 2 and 3). The main functions of this code include:

- Analog-to-digital conversion of thermocouple voltages and internal temperature

- Normalization of thermocouple and ambient temperature data

- 27-byte packet assembly

- Wireless data transmission via the Nordic TRF-2.4G wireless transceiver

Other operations performed by this software include capturing and transmitting the system status including thermocouple type in use, packet count, and overall system status. Figure 9 shows the flow of the program from a high-level perspective.

Figure 9: TCA Microcontroller Software Flowchart

#### RF Repeater

The MSP430F149 Microcontroller on the RFR executes the C-code shown in Listing 4 of Appendix II (associated header files are shown in Listings 2 and 5). The main functions of this code include:

- Receiving data packets from the TCA

- Responding to requests from the PCIA

- Forwarding data onto the PCIA upon request

- General communication with the PCIA

Figure 10 shows the flow of the program from a high-level perspective.

Figure 10: RFR Microcontroller Software Flowchart

#### PC Interface Assembly

The MSP430F149 Microcontroller on the PCIA executes the C-code shown in Listing 3 of Appendix II. The main functions of this code include:

- Communication between RF Repeater array

- Receiving data packets from the RF Repeaters

- Forwarding data onto the PC via a serial-to-USB interface

Figure 11 shows the flow of the program from a high-level perspective.

Figure 11: PCIA Microcontroller Software Flowchart

#### USB Data Capture

The user’s PC will execute the C-code shown in Listing 7 of Appendix II (associated header file is shown in Listing 8) in order to capture data from the USB port. The main functions of this code include:

- Receive and interpret data on the USB port

- Format and print the data to the screen in real time

- Format and print the data to two different files (one for normal use, one for backup)

- Recover from unexpected USB interruptions

Figure 12 shows an example of the execution of this program. The USB data capture software was designed to handle the possibility of a disconnection with the USB device. During such an event, the program notifies the user of the error, and waits for reconnection, at which point data capture resumes normally.

Figure 12: USB Data Capture software execution

As shown in Figure 12, the USB data capture software indicates the following status information about each packet:

- “Packet #” – The USB data capture program assigns a number to each packet it receives.

- “TCA count” – The TCA assigns a number (0 through 99) to each packet it sends. This makes it possible to determine the number of missed packets by comparing “Packet #” (modulo 100) with “TCA count.”

- “From RFR#” – When the PCIA forwards a packet on to the PC, it tells the USB data capture software which RFR sent that particular packet. This may be useful in detecting problematic RFRs, in determining the number of RFR modules necessary to achieve a desired miss rate, and in establishing the need to reposition the RFR array.

- “TC type” – Every so often the TCA will execute a subroutine to determine which thermocouple type is in use. This allows the user to change types during data capture. This status field represents the thermocouple type currently in use.

- “Sys stat” – The TCA also communicates a one-bit general system status that is displayed in this field (0 = “system ok”, 1 = “system not ok”).

#### PC Graphical User Interface

The PC GUI is implemented as a Microsoft Excel File called kilnTempvX.X.xls, where “X.X” is the version number. The main features of this GUI include:

- Real-time temperature plotting

- Thermocouple reference junction compensation

- Automated data importation

- Semi-automated linear system calibration

- File protection (allows the spreadsheet to act as an executable file)

- Data archiving and time-stamping

Figures 13.0 through 13.2 show images from the PC GUI. Figure 13.0 is an image of temperature data in a tabular format. Figure 13.1 is an image of temperature data in a graphical format. Figure 13.2 shows the semi-automated calibration functionality.

Figure 13.0: PC GUI – Tabular data view

Figure 13.1: PC GUI – Graphical data view

Figure 13.2: PC GUI – Calibration sheet

##### Cold-Junction Compensation in Software

The PC GUI handles the reference-junction compensation that is necessary when interpreting thermocouple measurements. Because thermocouples can only measure a temperature differential (between the measuring end and the reference end), steps must be taken to reference the non-measuring end of the thermocouple.

One way of accomplishing this is by submerging the reference junction in an ice bath. This will maintain that the temperature difference between the two ends is, in fact, the temperature of the measuring end.

A more practical method of compensation involves an alternate temperature sensor (i.e. a thermistor or a temperature-sensing IC). By combining the thermocouple voltage with the reference junction temperature in the manner depicted in Figure 14, the correctly compensated temperature can be achieved.

Figure 14: Thermocouple temperature generation flowchart

The PC GUI executes this data processing automatically. However, it relies on accurate thermocouple voltage and ambient temperature data. Accumulating errors in the processes of amplification, analog-to-digital conversion, digital-to-analog conversion (in software), and attenuation (in software) can skew the accuracy of the temperature measurements.

### Testing and Verification

Design specifications and the overall functionality of the system were tested and verified by a series of test fixtures, first with isolated modules, and then with the complete system. The architectures of these test fixtures are detailed below.

#### Temperature Capture Assembly

Many test fixtures were designed and implemented to test and verify the TCA. The first test fixture was designed to test the hardware and software for temperature data capture and processing. The TCA was assembled with an FTDI USB Adapter instead of a Nordic wireless transceiver so that captured data could be written directly to a PC screen. Temperature data capture was tested and verified with the use of several reference temperatures. The actual temperature data was calculated manually from the digitized thermocouple voltages transmitted by the TCA using thermocouple conversion polynomials. This TCA test fixture verified the temperature data acquisition and digitization functionality of the TCA.

Another test fixture was then designed and implemented to test the Wireless transmission functionality of the TCA. The TCA was assembled completely and a wireless receiver circuit was constructed to receive the data being transmitted by the TCA. This receiver utilized an FTDI USB Adapter to store received data to the PC. The TCA was then run with software very similar to that of the final version. Temperature data was captured and transmitted to the receiver. The test fixture succeeded and helped verify the TCA as a whole.

#### RF Repeater

The RF Repeater design was partially tested in the second of two test fixtures for the TCA. The Nordic wireless transceiver and the MSP430 microcontroller were assembled together along with an FTDI USB adapter to allow the received data to be displayed by a PC. The receive portion of the RFR software was tested and verified by this test fixture.

Several experiments were conducted to determine optimal Nordic configurations. These experiments evaluated variables such as address length, checksum length, packet length, etc. The conclusions of this experiment lead to the packet structure shown in Figure 15 below.

| System status | Ambient temperature | TC 0 | . . . | TC 15 |
| --- | --- | --- | --- | --- |
| 215 | 204 | 203 | 192 | 191 | 180 | 179 | 12 | 11 | 0 |
| Byte 26 | Byte 25 | Byte 24 | Byte 23 | . . . | Byte 1 | Byte 0 |
| 215 | 208 | 207 | 200 | 199 | 192 | 191 | 184 | 183 | 16 | 15 | 8 | 7 | 0 |

Figure 15: Packet structure

The second test fixture for the RFR involved assembling the complete RFR module and connecting it to the PCIA module via an RS-485 interface. This test could not be performed until the PCIA was assembled.

#### PC Interface Assembly

The serial to USB interface portion of the PCIA, both in terms of the hardware connections and the segment of software necessary to enable this interface, was verified in the test fixtures for both the TCA and the RFR. The remaining portion of the PCIA that needed to be tested and verified was the hardware and software to enable communication between eight RFRs.

A test fixture was designed to test and verify both the PCIA and the RFR designs. A complete PCIA was assembled as well as one RFR module. These assemblies were connected via four twisted-pairs RS-485. The verified TCA was set to capture and transmit temperature data to the RFR. The RFR was programmed to receive this data, and, upon request, transmit it to the PCIA. The PCIA was then programmed to communicate the data it received to the PC via the USB interface. Once this simplified version of the RFR and PCIA software was verified, the complete version of both programs (including periodic RFR pinging, data status checking, and speed maximization) was tested and verified.

#### PC GUI

The PC GUI “kilnTempvX.X” was tested during construction by using a static data file as the test input and manipulating the contents of this file to test and verify all the features and functionality of the GUI, such as system status notifications and data importation.

The PC GUI was later verified by running it with actual real-time dynamic data and iterating through all boundary conditions and possible improper use. The misuse and error handling was made robust in anticipation of an end user that is not familiar with this particular type of graphical interface.

#### Complete System

The complete system was tested and verified by connecting all three assemblies and running the PC data capture and display software. To test the accuracy of the thermocouple measurements, several tests were performed.

First, thermocouples we placed near a heat source and allowed to stabilize. After the temperatures had stabilized, the TCA board was placed near the heat source as well so that the MSP430 microcontroller on the assembly would begin to heat up. In order for the design to be functional and accurate, the thermocouple temperature calculations in the PC GUI should remain constant despite the warming of the microcontroller (which signifies the warming of the inside of the heat-shielding box, a phenomenon that is sure to take place as the TCA passes through a high-temperature kiln). The test was successful and the thermocouple temperatures remained constant.

Next, the accuracy of the thermocouple measurements was tested. Several reference temperatures were used to test the thermocouple measurement accuracy. A digital thermometer was used to measure the temperature of various heat sources to the nearest tenth of a degree Celsius. In addition, a thermocouple simulator was used to generate voltages corresponding to a wide range of temperatures.

Deviations between actual and measured temperature were offset by a linear calibration of the system (accomplished in software). After calibration, measured temperatures were observed within one or two degrees of the actual temperature throughout most of the range of a K-type thermocouple (room temperature to 1200 (C). The internal temperature sensor on the Microcontroller was also calibrated in software using two measurement points and linear calibration.

# Final Product

The final prototype is a fully functional system that is accurate, robust, and user friendly. The prototype is tailored for industrial process monitoring in the ceramics industry and functions nicely according to the specifications that correspond to that application. It is also useful in many other environments and is designed to be reasonably versatile.

#### Performance

The measured performance specifications of the completed design are presented in Table 4 below.

Table 4: System specifications

| Requirement number | Parameter | Conditions | Value | Unit |
| --- | --- | --- | --- | --- |
|  |  |  | Min | Nominal | Max |  |
| 1 | Detectable temperature | B-type | RT |  | 1820 | Celsius |
|  |  | C-type | RT |  | 2320 | Celsius |
|  |  | J-type | RT |  | 1200 | Celsius |
|  |  | K-type | RT |  | 1372 | Celsius |
|  |  | R-type | RT |  | 1768 | Celsius |
|  |  | S-type | RT |  | 1768 | Celsius |
|  |  | T-type | RT |  | 400 | Celsius |
| 2 | Transmission period |  | Reconfigurable for any period in the range [0.07 sec., 32.8 min.] with resolution 0.03 sec. | seconds per packet |
| 3 | Transmit-side supply voltage | Rechargeable NIMH batteries |  | 4.8 |  | Volts |
| 4 | Transmit-side power consumption | Max load (sample period ( 0.06 sec) |  |  | 0.037 | Watts |
| 5 | Transmission frequency |  | 2.4 | 2.4 | 2.524 | GHz |
| 6 | Wireless transmission range | Clear line of sight |  |  | 15 | meters |
| 7 | Temperature resolution | After calibration |  | 1 | 3 | Celsius |
| 8 | Electronics box width |  | 3 |  |  | cm |
| 9 | Electronics box height |  | 1.5 |  |  | cm |
| 10 | Electronics box length |  | 5 |  |  | cm |
| 11 | Ambient temperature inside electronics box |  |  |  | 100 | Celsius |
| 12 | Duration in kiln |  | 45 |  | 540 | minutes |
| 13 | RFR-PCIA separation |  |  |  | 4000 | feet |
| 14 | Packet miss rate | Single RFR, 1 foot TX distance, 2 sec. TX period |  | 2% |  |  |

After calibrating the system with a thermocouple simulator, measurement accuracy was observed to be in the range of one to two degrees Celsius. The system performance in terms of power consumption, sample rate, and usable temperature range significantly exceeded the original requirements.

#### Cost Estimation

The final cost of a prototype is detailed in Table 5. As the table shows, the maximum cost of the prototype is approximately $1,196.70. Although this price appears to be high, almost 75% of the total is comprised of the thermocouples alone. The type of thermocouples used in the cost calculation (R-type) contains platinum and were chosen because they are the type of thermocouple that would be used in the ceramics kiln application. Using different, cheaper thermocouple types would reduce the prototype cost significantly, but the range of measurable temperatures is determined by the type of thermocouple used.

It is difficult to find products with the same characteristics and application environments as this prototype. Honeywell International makes a line of Wireless Analog Input Transmitters that cost approximately $1190.00, very similar to the price of this prototype. The price of this product, however, does not include the temperature measuring device(s) necessary for its application. For the extreme temperature range that this product is designed for, temperature measurement devices are limited almost exclusively to R or S type thermocouples. As mentioned above, these thermocouples are relatively expensive and when added to the cost of the Honeywell product, the price would increase significantly. So, an existing product like the one offered by Honeywell International would not only be more expensive (after the purchase of the temperature measurement devices), but it is also unclear whether it provides the same functionality and features that this system provides.

Table 5: Prototype Cost

# Study Organization

Table 6 and Figure 16 below show the Gantt chart used in the preliminary stages of the project design. Due to changing customer requirements, unexpected difficulties, and delayed parts acquisition, the project task schedule was eventually modified to that shown in Table 7 and Figure 17.

Table 6: Preliminary Task Schedule

Figure 16: Preliminary Gantt Chart

Table 7: Final Task Schedule

Figure 17: Final Gantt Chart

# References and Acknowledgements

Table 8 lists the various resources that have been referenced during the development of this product.

Table 8: References and acknowledgements

| Reference | Description | Reference capacity | Link to resource |
| --- | --- | --- | --- |
| Dr. Karl Gugel | Professor and owner of Digital Control Lab | Technical direction | gugel@ecel.ufl.edu |
| Tsang Wei Huang | Graduate student and Teaching Assistant | Technical support | twhuang@ufl.edu |
| Grzegorz Cieslewski | Graduate student, Teaching Assistant, Research Assistant | Technical support | grzegorz@ufl.edu |
| Spark Fun Electronics | Electronics distributor and development board manufacturer | Data sheets, product features, and pricing information for various transceivers and microcontrollers | www.sparkfun.com |
| Analog Devices | Integrated Circuit (IC) manufacturer | Data sheets, product features, and pricing information for various amplifiers, voltage regulators, and DC-to-DC converters | http://www.analog.com |
| Maxim Integrated Products | Integrated Circuit (IC) manufacturer | Data sheets, product features, and pricing information for various ICs | http://www.maxim-ic.com |
| US Department of Commerce | National Institute of Standards and Technology (NIST) | Coefficients for thermocouple reference-junction compensation polynomials | http://srdata.nist.gov/its90/download/download.html |

# APPENDIX I: Bill of Materials

Table 9.0: TCA bill of materials

Table 9.1: RFR bill of materials

Table 9.2: PCIA bill of materials

# APPENDIX II: Source Code

## TCA: TCA_software.c

//******************************************************************************

//  File: TCA_software.c

//  Authors: Casey Morrison, Dean Morrison

//  Date Created:   03/07/2005

//  Date Modified:  04/09/2005

//

//  Description: This program handles the analog-to-digital conversions, packet

//               assembly, and packet transmission for the TCA. Included in each

//               packet is information about the system status, the type of

//               thermocouple being used for the given time period, 16 thermocouple

//               samples, and an internal temperature measurement (as well as other

//               status information).

//

//

//                 MSP430F149

//             -----------------

//            |                 |

//            |              A0 |<---- TCVoltage

//            |              A1 |<---- GainControl_B

//            |              A2 |<---- GainControl_C

//            |              A3 |<---- GainControl_J

//            |              A4 |<---- GainControl_K

//            |              A5 |<---- GainControl_R

//            |              A6 |<---- GainControl_S

//            |              A7 |<---- GainControl_T

//            |                 |

//            +-----------------+

//

//

//******************************************************************************

#include  "msp430x14x.h"            // Standard MSP430 equations

#include  "kilnTemp_defs.h"         // System-wide definitions

#include  "TCA_wireless_protocol.h" // Wireless protocol definitions

// Function prototypes

void initSys(void);

void initTRF(void);

void TX_TRF_mode(void);

void clkAddrBytes(unsigned int address_width);

void clkDataBytes(unsigned int data_width);

void Set_DCO (void);

unsigned int Normalize(unsigned int results[], int length);

void acquireData(void);

void updateThermocoupleType(void);

void clearPacket(void);

void delay(int delay_loops);

// Function prototypes for USB configuration only

void configUART0(void);

void sendUSB (unsigned int data_width);

// Data arrays

static unsigned int Tresults[16];

static unsigned int T0results[NUM_OF_RESULTS];

static unsigned int T1results[NUM_OF_RESULTS];

static unsigned int T2results[NUM_OF_RESULTS];

static unsigned int T3results[NUM_OF_RESULTS];

static unsigned int T4results[NUM_OF_RESULTS];

static unsigned int T5results[NUM_OF_RESULTS];

static unsigned int T6results[NUM_OF_RESULTS];

static unsigned int T7results[NUM_OF_RESULTS];

static unsigned int T8results[NUM_OF_RESULTS];

static unsigned int T9results[NUM_OF_RESULTS];

static unsigned int T10results[NUM_OF_RESULTS];

static unsigned int T11results[NUM_OF_RESULTS];

static unsigned int T12results[NUM_OF_RESULTS];

static unsigned int T13results[NUM_OF_RESULTS];

static unsigned int T14results[NUM_OF_RESULTS];

static unsigned int T15results[NUM_OF_RESULTS];

static unsigned int A0results[NUM_OF_RESULTS];

static unsigned int A1results[NUM_OF_RESULTS];

static unsigned int A2results[NUM_OF_RESULTS];

static unsigned int A3results[NUM_OF_RESULTS];

static unsigned int A4results[NUM_OF_RESULTS];

static unsigned int A5results[NUM_OF_RESULTS];

static unsigned int A6results[NUM_OF_RESULTS];

static unsigned int A7results[NUM_OF_RESULTS];

static unsigned int A8results[NUM_OF_RESULTS];

static unsigned int A9results[NUM_OF_RESULTS];

static unsigned int A10results[NUM_OF_RESULTS];

static unsigned int A11results[NUM_OF_RESULTS];

static unsigned int A12results[NUM_OF_RESULTS];

static unsigned int A13results[NUM_OF_RESULTS];

static unsigned int A14results[NUM_OF_RESULTS];

static unsigned int A15results[NUM_OF_RESULTS];

static unsigned int Tnormalized;

static unsigned int Anormalized[16];

// Packet data arrays

static unsigned int Byte[PACKET_SIZE];

static unsigned int status_batt;

static unsigned int status_count;

static unsigned int status_TC;

static unsigned int status_sys;

static unsigned int temp;

static unsigned int TC[16];

static unsigned int configByte[15];

// Global variables

unsigned int data_ready = FALSE;

unsigned int conversion_number = 0;

unsigned int sleepNumber = 0;

unsigned int packet_number = 0;

unsigned int TC_type = R_TYPE;

//------------------------------------------------------------------------------

void main(void) {

//------------------------------------------------------------------------------

WDTCTL = WDTPW+WDTHOLD;               // Stop watchdog timer

// Configure MCLK (~1.9MHz)

BCSCTL1 |= DIVA_3;                    // ACLK= LFXT1CLK/8

Set_DCO();                            // Set DCO

// Initialize the MSP430 system

initSys();

// Delay 1

delay(DELAY1);

//-------------------------------------------------------------------

// WIRELESS CONFIGURATION ONLY

// Initialize the TRF-2.4G

initTRF();

//-------------------------------------------------------------------

// Delay 2

delay(DELAY2);

//-------------------------------------------------------------------

// WIRELESS CONFIGURATION ONLY

// Configure for TX mode

TX_TRF_mode();

//-------------------------------------------------------------------

// Delay 3

delay(DELAY3);

// Set up sleep timer

CCTL0 = CCIE;                         // CCR0 interrupt enabled

CCR0 = SLEEP_AMT;                     // Number of SMCLK cycles the MSP will sleep for

// Set up analog multiplexer control bits (Port 1)

P1OUT  = 0x00;                        // Clear P1.0-P1.3 --> start with TC[0]

P1DIR |= 0x0F;                        // Configure P1.0-P1.3 for output

// Set up Gain Control inputs

P6SEL &= 0x01;                        // Configure P6.1-P6.7 for I/O

P6DIR &= 0x01;                        // Configure P6.1-P6.7 for input

// Data acquisition and transmission

packet_number = 0;

for(;;) {

clearPacket();

if(packet_number%CYCLES_BTW_GAIN == 0) {

// Resample gain control channels to update thermocouple type

updateThermocoupleType();

}

// Sample thermocouples and internal temperature and assemble packet

acquireData();

// Transmit data

P4OUT |= TX_LED;                    // Toggle TX LED

P2OUT |= TRF_CE;                    // Enable module 1: active mode

//-------------------------------------------------------------------

// WIRELESS CONFIGURATION ONLY

// Clock in ADDR_W number of address bytes

// NOTE: If you do not want all address bytes to be equal,

//       then you must manually clock in ADDR_TXa, ADDR_TXb, etc.

clkAddrBytes(ADDR_W);

// Clock in data

clkDataBytes(DATA_W);

//-------------------------------------------------------------------

//-------------------------------------------------------------------

// USB CONFIGURATION ONLY

// Send data via USB

//sendUSB(DATA_W);

//-------------------------------------------------------------------

P2OUT &= ~TRF_CE;                // Setting CE low completes transmit

P4OUT &= ~TX_LED;                // Indicate end of transmission

// Sleep to save power

sleepNumber = 0;

P4OUT &= ~TSA_ACT_LED;            // Indicate that TSA is asleep

TACTL = TASSEL_2 + MC_1;          // SMCLK, upmode

_BIS_SR(LPM0_bits + GIE);         // Enter LPM0 w/ interrupt

}

} // end main()

// *****************************************************************************

// Subroutines                                                                 *

// *****************************************************************************

//------------------------------------------------------------------------------

void delay(int delay_loops) {   // Generic delay loop

//------------------------------------------------------------------------------

int index = DELAY_AMT;

int loop;

for(loop = 0; loop < delay_loops; loop += 1) {

while(index > 0) {

--index;

}

index = DELAY_AMT;

}

}// end delay()

//------------------------------------------------------------------------------

void initSys(void) {   // Initialize MSP430 System

//------------------------------------------------------------------------------

// Default configurations for I/O ports

P1SEL = 0x00;                         // configure P1 for I/O

P1OUT = 0x00;                         // Clear P1.x

P1DIR = 0xFF;                         // Configure P1 for output

P2SEL = 0x00;                         // configure P2 for I/O

P2OUT = 0x00;                         // Clear P2.x

P2DIR = 0xFF;                         // Configure P2 for output

P3SEL = 0x00;                         // configure P3 for I/O

P3OUT = 0x00;                         // Clear P3.x

P3DIR = 0xFF;                         // Configure P3 for output

P4SEL = 0x00;                         // configure P4 for I/O

P4OUT = 0x00;                         // Clear P4.x

P4DIR = 0xFF;                         // Configure P4 for output

P4OUT |= TSA_ACT_LED;                 // Turn TSA_Active on

P5SEL = 0x00;                         // configure P5 for I/O

P5OUT = 0x00;                         // Clear P5.x

P5DIR = 0xFF;                         // Configure P5 for output

P6SEL = 0x00;                         // configure P6 for I/O

P6OUT = 0x00;                         // Clear P6.x

P6DIR = 0xFF;                         // Configure P6 for output

//-------------------------------------------------------------------

// USB CONFIGURATION ONLY

// Set up UART0

//configUART0();

//-------------------------------------------------------------------

_EINT();                              // Enable interrupts

}// end initSys()

//------------------------------------------------------------------------------

void Set_DCO (void) {   // Set DCO to selected frequency

//------------------------------------------------------------------------------

#define DELTA 488                       // Target DCO = DELTA*(4096) ~= 2MHz

unsigned int Compare, Oldcapture = 0;

CCTL2 = CM_1 + CCIS_1 + CAP;            // CAP, ACLK

TACTL = TASSEL_2 + MC_2 + TACLR;        // SMCLK, cont-mode, clear

while (1) {

while (!(CCIFG & CCTL2));           // Wait until capture occured

CCTL2 &= ~CCIFG;                    // Capture occured, clear flag

Compare = CCR2;                     // Get current captured SMCLK

Compare = Compare - Oldcapture;     // SMCLK difference

Oldcapture = CCR2;                  // Save current captured SMCLK

if (DELTA == Compare) break;        // If equal, leave "while(1)"

else if (DELTA < Compare) {

DCOCTL--;

if (DCOCTL == 0xFF) {           // DCO is too fast, slow it down

if (!(BCSCTL1 == (XT2OFF + DIVA_3)))

BCSCTL1--;              // Did DCO role under?, Sel lower RSEL

}

}

else {

DCOCTL++;                       // DCO is too slow, speed it down

if (DCOCTL == 0x00) {

if (!(BCSCTL1 == (XT2OFF + DIVA_3 + 0x07)))

BCSCTL1++;              // Did DCO role over? Sel higher RSEL

}

}

}

CCTL2 = 0;                              // Stop CCR2

TACTL = 0;                              // Stop Timer_A

}// end Set_DCO()

//------------------------------------------------------------------------------

void configUART0(void) {    // This method is for USB configuration only

//------------------------------------------------------------------------------

P3SEL |= 0x30;                        // P3.4,5 = USART0 TXD/RXD

ME1 |= UTXE0;                         // Enable USART0 TXD

UCTL0 |= CHAR;                        // 8-bit character, SWRST = 1

UTCTL0 |= SSEL1 + SSEL0 + URXSE;      // UCLK = SMCLK, start edge detect

UBR00 = 0xD0;                         // 9600 from 2Mhz

UBR10 = 0x00;

UMCTL0 = 0x00;                        // No modulation

UCTL0 &= ~SWRST;                      // Initialize USART state machine

//IE1 |= URXIE0;                        // Enable USART0 RX interrupt

}// end configUART()

//------------------------------------------------------------------------------

void sendUSB (unsigned int data_width) {    // For USB configuration only

//------------------------------------------------------------------------------

// Clear data_ready flag

data_ready = FALSE;

// Transmit packet byte-by-byte

int i;

for(i = data_width - 1; i >= 0; i -= 1) {

while(!(IFG1 & UTXIFG0));           // USART0 TX buffer ready?

TXBUF0 = Byte[i];

}

// Increment packet number (modulo MAX_PACKET_NUMBER)

packet_number = (packet_number + 1)%MAX_PACKET_NUMBER;

}// end sendUSB()

//------------------------------------------------------------------------------

void initTRF(void) {    // Initialize the TRF-2.4G system

//------------------------------------------------------------------------------

/*

description:  Initializes the SPI port for TRF module and configures for shock-

burst mode. default is active transmit mode.

------------+                      +---------

P3.1/SIMO0|--------------------->|Data1

MSP430     P3.2/SOMI0|<---------------------|Data2        TRF-2.4G

P3.3/UCLK0|--------------------->|CLK1=CLK2

P2.4|--------------------->|CE

P2.5|--------------------->|CS

P2.0|<---------------------|DR2  (this is so you can use

|                      |      Port 2 as interruptable pin)

------------+                      +---------

Active = /CS +  CE

Config =  CS + /CE

Stdby  = /CS + /CE

*/

P2DIR &= ~TRF_DR2;          // Configure Port 2.0 for input direction

P2OUT &= ~(TRF_CE+TRF_CS);  // Clear output on P2.4, P2.5

P2DIR |= TRF_CE+TRF_CS;     // Set P2.4, P2.5 to output direction

P3SEL |= 0x0E;              // Select SPI option on P3.1, P3.2, P3.3

U0CTL = CHAR+SYNC+MM+SWRST; // 8-bit, SPI, Master

U0TCTL |= CKPH+SSEL1+STC;   // Polarity __/--, SMCLK, 3-wire

U0BR1 = BAUDDIV0H;          // SPI0CLK = SMCLK/BAUDRATE0

U0BR0 = BAUDDIV0L;

U0MCTL = 0x000;             // No modulation

ME1 |= USPIE0;              // Module enable

U0CTL &= ~SWRST;            // SPI enable

// Assemble bytes of configuration word

configByte[0]  = (DATA_W*8) & 0xFF;   // 0x08

configByte[1]  = (DATA_W*8) & 0xFF;   // 0x08

configByte[2]  = ADDR_RXa   & 0xFF;   // 0x01

configByte[3]  = ADDR_RXb   & 0xFF;   // 0x01

configByte[4]  = ADDR_RXc   & 0xFF;   // 0x01

configByte[5]  = ADDR_RXd   & 0xFF;   // 0x01

configByte[6]  = ADDR_RXe   & 0xFF;   // 0xC8

configByte[7]  = 0x01       & 0xFF;   // 0x01

configByte[8]  = 0x01       & 0xFF;   // 0x01

configByte[9]  = 0x01       & 0xFF;   // 0x01

configByte[10] = 0x01       & 0xFF;   // 0x01

configByte[11] = 0x01       & 0xFF;   // 0x01

configByte[12] = (((ADDR_W*8)<<2) | (CRC_L<<1) | (CRC_EN)) & 0xFF;  // 0x43

configByte[13] = ((RX2_EN<<7) | (CM<<6) | (RFDR_SB<<5) | (XO_F<<2) | (RF_PWR)) & 0xFF;  // 0xCF

configByte[14] = (((RF-2400+8)<<1) | (AM_TX)) & 0xFF; // 0x74

P2OUT |= TRF_CS;                    // Enable TRF config mode

// Transmit configuration bytes

unsigned int TX_index;

for(TX_index = 0; TX_index <= 14; TX_index += 1) {

while(!(IFG1 & UTXIFG0));       // USART0 TX buffer ready?

TXBUF0 = configByte[TX_index];

}

while(!(U0TCTL & TXEPT));           // Wait til TXreg is empty

P2OUT &= ~TRF_CS;                   // Disable TRF config mode

}// end initTRF()

//------------------------------------------------------------------------------

void TX_TRF_mode(void) {    // Configure system for transmit

//------------------------------------------------------------------------------

U0TCTL |= CKPH;                     // Set SPI Polarity __/--

P2OUT |= TRF_CS;                    // Turn on configuration mode

while(!(IFG1 & UTXIFG0));           // USART0 TX buffer ready?

TXBUF0 = ((RF-2400+8)<<1) | (AM_TX);// 0x74;

while(!(U0TCTL & TXEPT));           // Wait til TXreg is empty

P2OUT &= ~TRF_CS;                   // Turn off config mode

}// end TX_TRF_mode

//------------------------------------------------------------------------------

void clearPacket(void) {

//------------------------------------------------------------------------------

// Clear the packet

unsigned int i;

for(i = 0; i < PACKET_SIZE; i += 1) {

Byte[i] = 0;

}

status_batt   = 0;

status_count  = 0;

//status_TC     = 0;

status_sys    = 0;

temp          = 0;

unsigned int j;

for(j = 0; j < 16; j += 1) {

TC[j] = 0;

}

} // end clearPacket()

//------------------------------------------------------------------------------

void clkAddrBytes(unsigned int address_width) { // Clock in address bytes

//------------------------------------------------------------------------------

int i;

for(i = 0; i < address_width; i += 1) {

while(!(IFG1 & UTXIFG0));           // USART0 TX buffer ready?

TXBUF0 = ADDR_BYTE;

}

}// end clkAddrBytes()

//------------------------------------------------------------------------------

void clkDataBytes(unsigned int data_width) {  // Clock in data bytes

//------------------------------------------------------------------------------

// Clear data_ready flag

data_ready = FALSE;

int i;

for(i = data_width - 1; i >= 0; i -= 1) {

while(!(IFG1 & UTXIFG0));           // USART0 TX buffer ready?

TXBUF0 = Byte[i];

}

while(!(U0TCTL & TXEPT));               // Wait until TXreg is empty

// Increment packet number (modulo MAX_PACKET_NUMBER)

packet_number = (packet_number + 1)%MAX_PACKET_NUMBER;

}// end clkDataBytes()

//------------------------------------------------------------------------------

void updateThermocoupleType(void) {

//------------------------------------------------------------------------------

/*

MSP430F149

+-----------------+

|              A0 |<---- TCVoltage

|              A1 |<---- GainControl_B

|              A2 |<---- GainControl_C

|              A3 |<---- GainControl_J

|              A4 |<---- GainControl_K

|              A5 |<---- GainControl_R

|              A6 |<---- GainControl_S

|              A7 |<---- GainControl_T

+-----------------+

*/

// Determine which thermocouple type is selected

//   Step 1: Read P6.1 through P6.7

unsigned int Port6;

Port6 = P6IN;

TC_type = UNDET_TYPE; // default

unsigned int GainControlError = FALSE;

if(Port6 & 0x02) {

// channel 1 (B_TYPE) on

TC_type = B_TYPE;

}

if(Port6 & 0x04) {

// channel 2 (C_TYPE) on

if(TC_type != 0) {

// multiple channels selected

GainControlError = TRUE;

}

else {

TC_type = C_TYPE;

}

}

if(Port6 & 0x08) {

// channel 3 (J_TYPE) on

if(TC_type != 0) {

// multiple channels selected

GainControlError = TRUE;

}

else {

TC_type = J_TYPE;

}

}

if(Port6 & 0x10) {

// channel 4 (K_TYPE) on

if(TC_type != 0) {

// multiple channels selected

GainControlError = TRUE;

}

else {

TC_type = K_TYPE;

}

}

if(Port6 & 0x20) {

// channel 5 (R_TYPE) on

if(TC_type != 0) {

// multiple channels selected

GainControlError = TRUE;

}

else {

TC_type = R_TYPE;

}

}

if(Port6 & 0x40) {

// channel 6 (S_TYPE) on

if(TC_type != 0) {

// multiple channels selected

GainControlError = TRUE;

}

else {

TC_type = S_TYPE;

}

}

if(Port6 & 0x80) {

// channel 7 (T_TYPE) on

if(TC_type != 0) {

// multiple channels selected

GainControlError = TRUE;

}

else {

TC_type = T_TYPE;

}

}

// Set thermocouple type

if(GainControlError == FALSE) {

status_TC = TC_type;

}

else {

status_TC = UNDET_TYPE;

status_sys = SYS_NOT_OK;

}

}// end updateThermocoupleType()

//------------------------------------------------------------------------------

void acquireData(void) {

//------------------------------------------------------------------------------

/*

MSP430F149

+-----------------+

|       A0(INCH_0)|<---- TCVoltage

|        (INCH_10)|<---+

|                 |    |

|    Internal_temp|----+

+-----------------+

*/

// Configure for two channels of conversions

// (one for TC conversions and one for internal temperature conversion)

data_ready = FALSE;                   // Reset data_ready flag

P6SEL = 0x01;                         // Enable A/D channel input P6.0

ADC12CTL0 = ADC12ON+MSC+SHT0_10+REFON;// ADC12ON --> Turn on ADC12

// SHT0_8  --> Sample-and-hold time = 256 clock cycles

// SHT0_10 --> Sample-and-hold time = 512 clock cycles

// REFON   --> Internal 1.5V reference for internal temp.

ADC12CTL1 = SHP+CONSEQ_1+CSTARTADD_0; // Use sampling timer, sequence-of-channels, single-conversion

conversion_number = 0;                // Start with 0th conversion, end with 15th

ADC12MCTL0 = INCH_0;                  // ref+=AVcc, channel = A0 (Thermocouple voltage)

ADC12MCTL1 = INCH_10+SREF_1+EOS;      // ref+=1.5V, channel = Internal temperature

ADC12IE = 0x02;                       // Enable ADC12IFG.1

ADC12CTL0 |= ENC;                     // Enable conversions

_EINT();                              // Enable interrupts

ADC12CTL0 |= ADC12SC;                 // Start conversion

_BIS_SR(LPM0_bits + GIE);             // Enter and stay in LPM0

while(data_ready == FALSE) {

// wait for data to be ready

}

}// end acquireData()

//------------------------------------------------------------------------------

unsigned int Normalize(unsigned int results[], int length) {

//------------------------------------------------------------------------------

int min_index = 0;

int max_index = 0;

unsigned int average = 0;

// find min

for (int i = 1; i < length; i++) {

if (results[i] < results[i-1]) min_index = i;

}

// find max

for (int i = 1; i < length; i++) {

if (results[i] > results[i-1]) max_index = i;

}

// average

for (int i = 0; i < length; i++) {

average += results[i];

}

average -= results[min_index];

average -= results[max_index];

average = average/(length - 2);

return average;

}// end Normalize()

//------------------------------------------------------------------------------

#pragma vector=ADC_VECTOR

__interrupt void ADC12ISR (void) {

//------------------------------------------------------------------------------

static unsigned int index = 0;

//

//ADC12CTL0 &= ~ENC;                 // Disable conversions

//ADC12CTL0 &= ~ADC12SC;             // Stop conversion

// Obtain conversion data

if(conversion_number == 0) {

A0results[index] = ADC12MEM0;     // Move A0 results, IFG is cleared

T0results[index] = ADC12MEM1;

}

else if(conversion_number == 1) {

A1results[index] = ADC12MEM0;     // Move A1 results, IFG is cleared

T1results[index] = ADC12MEM1;

}

else if(conversion_number == 2) {

A2results[index] = ADC12MEM0;     // Move A2 results, IFG is cleared

T2results[index] = ADC12MEM1;

}

else if(conversion_number == 3) {

A3results[index] = ADC12MEM0;     // Move A3 results, IFG is cleared

T3results[index] = ADC12MEM1;

}

else if(conversion_number == 4) {

A4results[index] = ADC12MEM0;     // Move A4 results, IFG is cleared

T4results[index] = ADC12MEM1;

}

else if(conversion_number == 5) {

A5results[index] = ADC12MEM0;     // Move A5 results, IFG is cleared

T5results[index] = ADC12MEM1;

}

else if(conversion_number == 6) {

A6results[index] = ADC12MEM0;     // Move A6 results, IFG is cleared

T6results[index] = ADC12MEM1;

}

else if(conversion_number == 7) {

A7results[index] = ADC12MEM0;     // Move A7 results, IFG is cleared

T7results[index] = ADC12MEM1;

}

else if(conversion_number == 8) {

A8results[index] = ADC12MEM0;     // Move A9 results, IFG is cleared

T8results[index] = ADC12MEM1;

}

else if(conversion_number == 9) {

A9results[index] = ADC12MEM0;    // Move A10 results, IFG is cleared

T9results[index] = ADC12MEM1;

}

else if(conversion_number == 10) {

A10results[index] = ADC12MEM0;    // Move A11 results, IFG is cleared

T10results[index] = ADC12MEM1;

}

else if(conversion_number == 11) {

A11results[index] = ADC12MEM0;    // Move A12 results, IFG is cleared

T11results[index] = ADC12MEM1;

}

else if(conversion_number == 12) {

A12results[index] = ADC12MEM0;    // Move A13 results, IFG is cleared

T12results[index] = ADC12MEM1;

}

else if(conversion_number == 13) {

A13results[index] = ADC12MEM0;    // Move A14 results, IFG is cleared

T13results[index] = ADC12MEM1;

}

else if(conversion_number == 14) {

A14results[index] = ADC12MEM0;    // Move A15 results, IFG is cleared

T14results[index] = ADC12MEM1;

}

else if(conversion_number == 15) {

A15results[index] = ADC12MEM0;    // Move A16 results, IFG is cleared

T15results[index] = ADC12MEM1;

}

else {

// This should not occur

status_sys = SYS_NOT_OK;

}

if(index >= (NUM_OF_RESULTS - 1)) {

// A single TC (or internal temp) has been sampled NUM_OF_RESULTS times

// Configure to convert next TC

conversion_number = (conversion_number + 1)%16;

if(conversion_number == 0) {

// A complete set of data has been acquired

// Set normalized values

Tresults[0]   = Normalize(T0results, NUM_OF_RESULTS);

Tresults[1]   = Normalize(T1results, NUM_OF_RESULTS);

Tresults[2]   = Normalize(T2results, NUM_OF_RESULTS);

Tresults[3]   = Normalize(T3results, NUM_OF_RESULTS);

Tresults[4]   = Normalize(T4results, NUM_OF_RESULTS);

Tresults[5]   = Normalize(T5results, NUM_OF_RESULTS);

Tresults[6]   = Normalize(T6results, NUM_OF_RESULTS);

Tresults[7]   = Normalize(T7results, NUM_OF_RESULTS);

Tresults[8]   = Normalize(T8results, NUM_OF_RESULTS);

Tresults[9]   = Normalize(T9results, NUM_OF_RESULTS);

Tresults[10]  = Normalize(T10results, NUM_OF_RESULTS);

Tresults[11]  = Normalize(T11results, NUM_OF_RESULTS);

Tresults[12]  = Normalize(T12results, NUM_OF_RESULTS);

Tresults[13]  = Normalize(T13results, NUM_OF_RESULTS);

Tresults[14]  = Normalize(T14results, NUM_OF_RESULTS);

Tresults[15]  = Normalize(T15results, NUM_OF_RESULTS);

Tnormalized   = Normalize(Tresults, 16);

Anormalized[0]  = Normalize(A0results, NUM_OF_RESULTS);

Anormalized[1]  = Normalize(A1results, NUM_OF_RESULTS);

Anormalized[2]  = Normalize(A2results, NUM_OF_RESULTS);

Anormalized[3]  = Normalize(A3results, NUM_OF_RESULTS);

Anormalized[4]  = Normalize(A4results, NUM_OF_RESULTS);

Anormalized[5]  = Normalize(A5results, NUM_OF_RESULTS);

Anormalized[6]  = Normalize(A6results, NUM_OF_RESULTS);

Anormalized[7]  = Normalize(A7results, NUM_OF_RESULTS);

Anormalized[8]  = Normalize(A8results, NUM_OF_RESULTS);

Anormalized[9]  = Normalize(A9results, NUM_OF_RESULTS);

Anormalized[10] = Normalize(A10results, NUM_OF_RESULTS);

Anormalized[11] = Normalize(A11results, NUM_OF_RESULTS);

Anormalized[12] = Normalize(A12results, NUM_OF_RESULTS);

Anormalized[13] = Normalize(A13results, NUM_OF_RESULTS);

Anormalized[14] = Normalize(A14results, NUM_OF_RESULTS);

Anormalized[15] = Normalize(A15results, NUM_OF_RESULTS);

// Assemble data packet

// Status word

//status_batt initialized to BATT_OK

status_count = packet_number;

//status_TC already set

//status_sys already set

// Data

temp  = Tnormalized;

unsigned int i;

for(i = 0; i < 16; i += 1) {

TC[i]  = Anormalized[i];

}

Byte[26] = (((status_batt << 7) & 0x80) | (status_count & 0x7F)) & 0xFF;

Byte[25] = ((((((status_TC << 1) & 0xE) | (status_sys & 0x1)) & 0x00F) << 4) | ((temp >> 8) & 0xF)) & 0xFF;

Byte[24] = temp & 0x0FF;

unsigned int tc_index = 0;

int j;

for(j = 23; j >= 2; j -= 3) {

Byte[j]   = (TC[tc_index] >> 4) & 0xFF;

Byte[j-1] = (((TC[tc_index] & 0x00F) << 4) | ((TC[tc_index+1] >> 8) & 0xF)) & 0xFF;

Byte[j-2] = TC[tc_index+1] & 0x0FF;

tc_index += 2;

}

// Transmit data

data_ready = 1;

// Reconfigure for next set of data

P1OUT = TC0;

ADC12CTL1 = SHP+CONSEQ_1+CSTARTADD_0;

}

else if(conversion_number == 1) {

P1OUT = TC1;

ADC12CTL1 = SHP+CONSEQ_1+CSTARTADD_0;

}

else if(conversion_number == 2) {

P1OUT = TC2;

ADC12CTL1 = SHP+CONSEQ_1+CSTARTADD_0;

}

else if(conversion_number == 3) {

P1OUT = TC3;

ADC12CTL1 = SHP+CONSEQ_1+CSTARTADD_0;

}

else if(conversion_number == 4) {

P1OUT = TC4;

ADC12CTL1 = SHP+CONSEQ_1+CSTARTADD_0;

}

else if(conversion_number == 5) {

P1OUT = TC5;

ADC12CTL1 = SHP+CONSEQ_1+CSTARTADD_0;

}

else if(conversion_number == 6) {

P1OUT = TC6;

ADC12CTL1 = SHP+CONSEQ_1+CSTARTADD_0;

}

else if(conversion_number == 7) {

P1OUT = TC7;

ADC12CTL1 = SHP+CONSEQ_1+CSTARTADD_0;

}

else if(conversion_number == 8) {

P1OUT = TC8;

ADC12CTL1 = SHP+CONSEQ_1+CSTARTADD_0;

}

else if(conversion_number == 9) {

P1OUT = TC9;

ADC12CTL1 = SHP+CONSEQ_1+CSTARTADD_0;

}

else if(conversion_number == 10) {

P1OUT = TC10;

ADC12CTL1 = SHP+CONSEQ_1+CSTARTADD_0;

}

else if(conversion_number == 11) {

P1OUT = TC11;

ADC12CTL1 = SHP+CONSEQ_1+CSTARTADD_0;

}

else if(conversion_number == 12) {

P1OUT = TC12;

ADC12CTL1 = SHP+CONSEQ_1+CSTARTADD_0;

}

else if(conversion_number == 13) {

P1OUT = TC13;

ADC12CTL1 = SHP+CONSEQ_1+CSTARTADD_0;

}

else if(conversion_number == 14) {

P1OUT = TC14;

ADC12CTL1 = SHP+CONSEQ_1+CSTARTADD_0;

}

else if(conversion_number == 15) {

P1OUT = TC15;

ADC12CTL1 = SHP+CONSEQ_1+CSTARTADD_0;

}

else {

// This should not occur

status_sys = SYS_NOT_OK;

}

}

if(data_ready == FALSE) {

// Restart conversions

ADC12CTL0 |= ENC;                 // Re-enable conversions

ADC12CTL0 |= ADC12SC;             // Restart conversion

}

// Increment results index (modulo NUM_OF_RESULTS)

index = (index+1)%NUM_OF_RESULTS;

_BIC_SR_IRQ(LPM0_bits);                   // Clear CPUOFF bit from 0(SR)

}// end ADC ISR

//------------------------------------------------------------------------------

#pragma vector=TIMERA0_VECTOR

__interrupt void Timer_A (void) {

// Check if we've slept long enough

if(++sleepNumber >= NUM_OF_SLEEPS) {

// Stop and clear Timer A

TACTL = TACLR;

// Wake up

_BIC_SR_IRQ(LPM0_bits);             // Clear CPUOFF bit from 0(SR)

P4OUT |= TSA_ACT_LED;               // Indicate that TSA is active

}

}

//------------------------------------------------------------------------------

## TCA: TCA_wireless_protocol.h

/******************************************************************************

File:   TCA_wireless_protocol.h

-----------------------------------------------------------------------------

Project        : Multi-channel Temperature Measurements with Telemetry

Author         : Casey T. Morrison, Dean R. Morrison

Created        : 03/16/2005

Last modified  : 04/11/2005

-----------------------------------------------------------------------------

Description : This is an include file for TCA_software.c that defines

defines constants for wireless communication.

-----------------------------------------------------------------------------

Copyright :

The author retains all rights to this application.  Please do

not distribute this code in any form, shape or way.

*******************************************************************************/

//------------------------------------------------------------------------------

// Constants

//------------------------------------------------------------------------------

#define   TRF_DR2     0x01                      // Data ready 2 (P2.0)

#define   TRF_DATA    0x02                      // Data channel 1 P3.1 or P5.1

#define   TRF_DATA2   0x04                      // Data channel 2 P3.2 or P5.2

#define   TRF_CLK     0x08                      // Clk            P3.3 or P5.3

#define   TRF_CE      0x10                      // Chip enable    P2.4

#define   TRF_CS      0x20                      // Chip select    P2.5

#define   UART_TX1    0x40                      // UART1 TX       P3.6

#define   UART_RX1    0x80                      // UART1 RX       P3.7

// Shockburst parameters:

// 1. Address length

#define   ADDR_W      2                         // Number of bytes for RX addrs (5 bytes max)

// 2. Receive channel address

#define   ADDR_BYTE   0x01

#define   ADDR_RXa    ADDR_BYTE                 // RX addr = 01.01.01.01.01

#define   ADDR_RXb    ADDR_BYTE

#define   ADDR_RXc    ADDR_BYTE

#define   ADDR_RXd    ADDR_BYTE

#define   ADDR_RXe    ADDR_BYTE

// 3. Transmit channel address

#define   ADDR_TXa    ADDR_BYTE                 // TX addr = 01.01.01.01.01

#define   ADDR_TXb    ADDR_BYTE

#define   ADDR_TXc    ADDR_BYTE

#define   ADDR_TXd    ADDR_BYTE

#define   ADDR_TXe    ADDR_BYTE

// 4. Data length

#define   DATA_W      27                        // Number of data bytes (25 bytes max?)

// 5. CRC

#define   CRC_L       1                         // '0' = 8-bit CRC (not recommended)

// '1' = 16-bit CRC (highly recommended)

#define   CRC_EN      1                         // '0' = disabled (not recommended)

// '1' = enabled (highly recommended)

// 5. General device parameters

#define   RX2_EN      1                         // '0' = one ch. receive

// '1' = two ch. receive

#define   CM          1                         // '0' = Direct mode

// '1' = ShockBurst mode (recommended)

#define   RFDR_SB     0                         // '0' = 250kbps

// '1' = 1Mbps

#define   XO_F        3                         // 16MHz crystal built-in (default)

#define   RF_PWR      3                         // 0dBm (changeable for smaller output and current consumption)

// 6. Active modes

#define   AM_TX       0                         // Transmit

#define   AM_RX       1                         // Receive

// 7. Frequency channel

//   2400MHz <= RF <= 2524MHz

//   receive chan 1 = RF    <--- never send data to

//   receive chan 2 = RF+8  <--- interested in!!

#define   RF          2450

//#define   RF          2467

// TX period settings

// Approximate equations for TX period (in seconds):

//    TX_period_in_seconds = 0.0317 * NUM_OF_SLEEPS + 0.0635

//    NUM_OF_SLEEPS = (TX_period_in_seconds - 0.0635)/0.0317

//    ***SELECT ONLY ONE DEFINITION FOR SLEEP_AMT AND NUM_OF_SLEEPS

// TX period ~= 0 seconds

//#define   SLEEP_AMT         10      // Cycles to sleep for each loop

//#define   NUM_OF_SLEEPS     1       // Number of sleep loops

// TX period ~= 2.00 seconds

#define   SLEEP_AMT         60000   // Cycles to sleep for each loop

#define   NUM_OF_SLEEPS     61     // Number of sleep loops

// TX period ~= 3.01 seconds

//#define   SLEEP_AMT         60000   // Cycles to sleep for each loop

//#define   NUM_OF_SLEEPS     93     // Number of sleep loops

// TX period ~= 4.01 seconds

//#define   SLEEP_AMT         60000   // Cycles to sleep for each loop

//#define   NUM_OF_SLEEPS     124     // Number of sleep loops

// TX period ~= 14.99 seconds

//#define   SLEEP_AMT         60000   // Cycles to sleep for each loop

//#define   NUM_OF_SLEEPS     471     // Number of sleep loops

// TX period ~= 30.02 seconds

//#define   SLEEP_AMT         60000   // Cycles to sleep for each loop

//#define   NUM_OF_SLEEPS     944     // Number of sleep loops

// TX period ~= 60 seconds

//#define   SLEEP_AMT         60000   // Cycles to sleep for each loop

//#define   NUM_OF_SLEEPS     1894    // Number of sleep loops

// Miscellaneous TCA definitions

#define   NUM_OF_RESULTS    12      // Number of samples for each TC for each packet

#define   CYCLES_BTW_GAIN   20      // Number of packets in between determining TC type

#define   MAX_PACKET_NUMBER 100     // Maximum packet count

#define   GAIN_CTL_MARGIN   1       // Minimum margin of error in determining TC type

#define   DELAY_AMT         5000    // Number of cycles in each delay loop

#define   DELAY1            0       // Number of delay loops for delay 1

#define   DELAY2            1       // Number of delay loops for delay 2

#define   DELAY3            1       // Number of delay loops for delay 3

#define   TSA_ACT_LED       1       // TSA_Active LED P4.0

#define   TX_LED            2       // Transmit LED   P4.1

## TCA, RFR, PCIA: kilnTemp_defs.h

/******************************************************************************

File:   kilnTemp_defs.h

-----------------------------------------------------------------------------

Project        : Multi-Channel Temperature Measurements with Telemetry

Author         : Casey T. Morrison, Dean R. Morrison

Created        : 03/08/2005

Last modified  : 04/11/2005

-----------------------------------------------------------------------------

Description : This is an include file for the Multi-Channel Temperature

Measurement with Telemetry system. It defines commonly used

constants.

-----------------------------------------------------------------------------

Copyright :

The author retains all rights to this application.  Please do

not distribute this code in any form, shape or way.

*******************************************************************************/

//------------------------------------------------------------------------------

// Constants

//------------------------------------------------------------------------------

// Thermocouple numbers

#define TC0           0x00   // Select Thermocouple 0

#define TC1           0x01   // Select Thermocouple 1

#define TC2           0x02   // Select Thermocouple 2

#define TC3           0x03   // Select Thermocouple 3

#define TC4           0x04   // Select Thermocouple 4

#define TC5           0x05   // Select Thermocouple 5

#define TC6           0x06   // Select Thermocouple 6

#define TC7           0x07   // Select Thermocouple 7

#define TC8           0x08   // Select Thermocouple 8

#define TC9           0x09   // Select Thermocouple 9

#define TC10          0x0A   // Select Thermocouple 10

#define TC11          0x0B   // Select Thermocouple 11

#define TC12          0x0C   // Select Thermocouple 12

#define TC13          0x0D   // Select Thermocouple 13

#define TC14          0x0E   // Select Thermocouple 14

#define TC15          0x0F   // Select Thermocouple 15

// Thermocouple types

#define UNDET_TYPE    0x000

#define B_TYPE        0x001

#define C_TYPE        0x002

#define J_TYPE        0x003

#define K_TYPE        0x004

#define R_TYPE        0x005

#define S_TYPE        0x006

#define T_TYPE        0x007

// Messages between RFRs and PCIA

#define PING_PCIA_RFR	    0xAA

#define PING_RFR_PCIA	    0x33

#define REQUEST_NEW_DATA    0xE4  // a request from the PCIA for new data from the RFR

#define NO_NEW_DATA	    0xCC  // RFR has no new data

#define DATA_RFR_PCIA	    0x96  // New Data Header

#define RESET_HND_REQUEST   0x15  // a command from the PCIA to all active RFRs to reset their have_new_data flags

#define RESET_HND_CONFIRM   0x77  // a response from the RFR confirming the reset of its have_new_data flag

// Baud rate settings for SPI

#define XCLK          9000000               // main = 9Mhz

#define BAUDRATE0     900000                // usart0 = 900kbps

#define BAUDRATE1     900000                // usart1 = 900kbps

#define BAUDDIV0      XCLK/BAUDRATE0

#define BAUDDIV0H     (BAUDDIV0>>8)&0x0FF   // upper baud

#define BAUDDIV0L     BAUDDIV0&0x0FF        // lower baud

#define BAUDDIV1      XCLK/BAUDRATE1

#define BAUDDIV1H     (BAUDDIV1>>8)&0x0FF   // upper baud

#define BAUDDIV1L     BAUDDIV1&0x0FF        // lower baud

// UART interrupt enable/disable

#define URXID1	      0xEF  // UART_1 RX interrupt disable mask (to disable RX interrupt: IE2 &= URXID1)

#define URXEID	      0xF7  // Mask to disable interrupts triggered by erroneous data

// RFR array

#define RFR_0	      0x00  // used to select the RX MUX

#define RFR_1	      0x01  // channel on the PCIA

#define RFR_2	      0x02

#define RFR_3	      0x03

#define RFR_4	      0x04

#define RFR_5	      0x05

#define RFR_6	      0x06

#define RFR_7	      0x07

// Packet size

#define PACKET_SIZE   27	// Packet size (in bytes)

// System status

#define SYS_OK        0

#define SYS_NOT_OK    1

// Battery status

#define BATT_OK       0

#define LOW_BATT      1

// Standard boolean

#define FALSE         0

#define TRUE          1

## RFR: RFR_software.c

//******************************************************************************

//  File: RFR_software.c

//  Authors: Dean Morrison, Casey Morrison

//  Date Created:  03/15/2005

//  Date Modified: 04/11/2005

//

//  Description: This program handles the communication between the TCA and the

//               PCIA. The RF Repeater receives the data that the TCA transmits

//               wirelessly. Then, the RF Repeater responds to data requests from

//               the PCIA by sending the requested data serially to the PCIA.

//

//                 MSP430F149                             Nordic TRF-2.4G

//             -----------------                         -----------------

//            |                 |                       |                 |

//            |            P1.0 |----> RX LED           |                 |

//            |            P1.1 |                       |                 |

//            |                 |                       |                 |

//            |            P2.1 |<----------------------| DR2             |

//            |            P2.2 |---------------------->| CE              |

//            |            P2.3 |---------------------->| CS              |

//            |                 |                       |                 |

//            |            P3.1 |---------------------->| DATA            |

//            |            P3.2 |<----------------------| DOUT2           |

//            |            P3.3 |----------------+----->| CLK1            |

//            |                 |                |----->| CLK2            |

//            |                 |                       |                 |

//            |            P3.6 |----> RS-485 TX        -----------------

//            |            P3.7 |<---- RS-485 RX

//            |                 |

//            |            P4.0 |----> Debug LED

//

//******************************************************************************

#include  "msp430x14x.h"            // Standard MSP430 equations

#include  "kilnTemp_defs.h"         // System-wide definitions

#include  "RFR_wireless_protocol.h" // Wireless protocol definitions

// Fuction prototypes

void initSys(void);

void delay(int delay_loops);

void Set_DCO (void);

void initTRF(void);

void initUART1(void);

void RX_TRF_mode(void);

void RX_TRF(void);

void clkAddrBytes(unsigned int address_width);

void wait(unsigned int wait_time);

void sendPCIA(void);

//------------------------------------------------------------------------------

//  Definitions

//------------------------------------------------------------------------------

// Global variables

static unsigned int recByte[PACKET_SIZE];

static unsigned int configByte[15];

unsigned int packet_number = 0;

static int HAVE_NEW_DATA = FALSE;     // flag representing whether or not the RFR has "new data"

//------------------------------------------------------------------------------

void main(void) {

//------------------------------------------------------------------------------

// Initialize the MSP430 system

initSys();

// Delay 1

delay(DELAY1);

// Initialize the TRF-2.4G

initTRF();

// Delay 2

delay(DELAY2);

// Initialize UART1

initUART1();

// Initialize wireless RX mode

RX_TRF_mode();

// Delay 3

delay(DELAY3);

P2OUT |= TRF_CE;                        // Enable active mode

// Receive loop

for(;;) {

// Wait for data

while(!(P2IN & TRF_DR2));

HAVE_NEW_DATA = TRUE;               // Set HAVE_NEW_DATA flag

// Retreive data

RX_TRF();

}

}// end main()

// *****************************************************************************

// Subroutines                                                                 *

// *****************************************************************************

//------------------------------------------------------------------------------

void initSys(void) {     //Initialize MSP430 System

//------------------------------------------------------------------------------

WDTCTL = WDTPW+WDTHOLD;               // Stop watchdog timer

BCSCTL1 |= DIVA_3;                    // ACLK= LFXT1CLK/8

Set_DCO();                            // Set DCO

// Default configurations for I/O ports

P1SEL = 0x00;                         // configure P1 for I/O

P1OUT = 0x00;                         // Clear P1.x

P1DIR = 0xFF;                         // Configure P1 for output

P2SEL = 0x00;                         // configure P2 for I/O

P2OUT = 0x00;                         // Clear P2.x

P2DIR = 0xFF;                         // Configure P2 for output

P3SEL = 0x00;                         // configure P3 for I/O

P3OUT = 0x00;                         // Clear P3.x

P3DIR = 0xFF;                         // Configure P3 for output

P4SEL = 0x00;                         // configure P4 for I/O

P4OUT = 0x00;                         // Clear P4.x

P4DIR = 0xFF;                         // Configure P4 for output

P5SEL = 0x00;                         // configure P5 for I/O

P5OUT = 0x00;                         // Clear P5.x

P5DIR = 0xFF;                         // Configure P5 for output

P6SEL = 0x00;                         // configure P6 for I/O

P6OUT = 0x00;                         // Clear P6.x

P6DIR = 0xFF;                         // Configure P6 for output

_EINT();                              // Enable interrupts

}// end initSys()

//------------------------------------------------------------------------------

void delay(int delay_loops) {   // Generic delay loop

//------------------------------------------------------------------------------

int index = DELAY_AMT;

int loop;

for(loop = 0; loop < delay_loops; loop += 1) {

while(index > 0) {

--index;

}

index = DELAY_AMT;

}

}// end delay()

//------------------------------------------------------------------------------

void Set_DCO (void) {                   // Set DCO to selected frequency

//------------------------------------------------------------------------------

#define DELTA 488                       // Target DCO = DELTA*(4096) ~= 2MHz

unsigned int Compare, Oldcapture = 0;

CCTL2 = CM_1 + CCIS_1 + CAP;            // CAP, ACLK

TACTL = TASSEL_2 + MC_2 + TACLR;        // SMCLK, cont-mode, clear

while (1) {

while (!(CCIFG & CCTL2));           // Wait until capture occured

CCTL2 &= ~CCIFG;                    // Capture occured, clear flag

Compare = CCR2;                     // Get current captured SMCLK

Compare = Compare - Oldcapture;     // SMCLK difference

Oldcapture = CCR2;                  // Save current captured SMCLK

if (DELTA == Compare) break;        // If equal, leave "while(1)"

else if (DELTA < Compare) {

DCOCTL--;

if (DCOCTL == 0xFF) {           // DCO is too fast, slow it down

if (!(BCSCTL1 == (XT2OFF + DIVA_3)))

BCSCTL1--;              // Did DCO role under?, Sel lower RSEL

}

}

else {

DCOCTL++;                       // DCO is too slow, speed it down

if (DCOCTL == 0x00) {

if (!(BCSCTL1 == (XT2OFF + DIVA_3 + 0x07)))

BCSCTL1++;              // Did DCO role over? Sel higher RSEL

}

}

}

CCTL2 = 0;                              // Stop CCR2

TACTL = 0;                              // Stop Timer_A

}// end Set_DCO()

//------------------------------------------------------------------------------

void initTRF(void) { // Initialize the TRF-2.4G system

//------------------------------------------------------------------------------

/*

Description: initializes the SPI port for TRF module and configures for shock-

burst mode. default is active receive mode.

------------+                      +---------

P3.1/SIMO0|--------------------->|Data1

MSP430     P3.2/SOMI0|<---------------------|Data2        TRF-2.4G

P3.3/UCLK0|--------------------->|CLK1=CLK2

P2.2|--------------------->|CE

P2.3|--------------------->|CS

P2.1|<---------------------|DR2  (this is so you can use

|                      |      Port 2 as interruptable pin)

P1.0|---> RX LED           |

------------+                      +---------

Active = /CS +  CE

Config =  CS + /CE

Stdby  = /CS + /CE

*/

P2DIR &= ~TRF_DR2;          // Configure Port 2.1 for input direction

P2OUT &= ~(TRF_CE+TRF_CS);  // Clear output on P2.2, P2.3

P2DIR |= TRF_CE+TRF_CS;     // Set P2.2, P2.3 to output direction

P3SEL |= 0x0E;              // Select SPI option on P3.1, P3.2, P3.3

U0CTL = CHAR+SYNC+MM+SWRST; // 8-bit, SPI, Master

U0TCTL |= CKPH+SSEL1+STC;   // Polarity __/--, SMCLK, 3-wire

U0BR1 = BAUDDIV0H;          // SPI0CLK = SMCLK/BAUDRATE0

U0BR0 = BAUDDIV0L;

U0MCTL = 0x000;             // No modulation

ME1 |= USPIE0;              // Module enable

U0CTL &= ~SWRST;            // SPI enable

// Assemble bytes of configuration word

configByte[0]  = (PACKET_SIZE*8) & 0xFF;   // 0x08

configByte[1]  = (PACKET_SIZE*8) & 0xFF;   // 0x08

configByte[2]  = ADDR_RXa   & 0xFF;   // 0x01

configByte[3]  = ADDR_RXb   & 0xFF;   // 0x01

configByte[4]  = ADDR_RXc   & 0xFF;   // 0x01

configByte[5]  = ADDR_RXd   & 0xFF;   // 0x01

configByte[6]  = ADDR_RXe   & 0xFF;   // 0xC8

configByte[7]  = 0x01       & 0xFF;   // 0x01

configByte[8]  = 0x01       & 0xFF;   // 0x01

configByte[9]  = 0x01       & 0xFF;   // 0x01

configByte[10] = 0x01       & 0xFF;   // 0x01

configByte[11] = 0x01       & 0xFF;   // 0x01

configByte[12] = (((ADDR_W*8)<<2) | (CRC_L<<1) | (CRC_EN)) & 0xFF;  // 0x43

configByte[13] = ((RX2_EN<<7) | (CM<<6) | (RFDR_SB<<5) | (XO_F<<2) | (RF_PWR)) & 0xFF;  // 0xCF

configByte[14] = (((RF-2400)<<1)  | (AM_RX)) & 0xFF; // 0x65

P2OUT |= TRF_CS;                    // Enable TRF config mode

// Transmit configuration bytes

unsigned int TX_index;

for(TX_index = 0; TX_index <= 14; TX_index += 1) {

while(!(IFG1 & UTXIFG0));       // USART0 TX buffer ready?

TXBUF0 = configByte[TX_index];

}

while(!(U0TCTL & TXEPT));           // Wait til TXreg is empty

P2OUT &= ~TRF_CS;                   // Disable TRF config mode

}// end initTrf()

//------------------------------------------------------------------------------

void initUART1(void) {   //

//------------------------------------------------------------------------------

/*

Description: UART port for communication with external module

(PCIA or FTDI) and configure for 9600 baud.

Application 1: MSP430-to-FTDI (dlp-usb232m14) communication

---------------+                      +---------

P3.6/UTXD1(34)|--------------------->|RXD

MSP430    P3.7/URXD1(35)|<---------------------|TXD        FTDI

|                      |

~RST/NMI|<---------------------|RESETO#

---------------+                      +---------

Application 2: MSP430 - RS485 communication

---------------+                      +---------

P3.6/UTXD1(34)|--------------------->|DI

MSP430    P3.7/URXD1(35)|<---------------------|RO         RS485

|                      |

---------------+                      +---------

*/

P3SEL |= UART_RX1 + UART_TX1;       // P3.6, P3.7 = USART1 RXD/TXD

ME2 |= UTXE1 + URXE1;               // Enable USART0 TXD/RXD

UCTL1 |= CHAR;                      // 8-bit characters

UTCTL1 = SSEL0;                     // UCLK = ACLK

UBR01 = 0x003;                      // 32k/9600 - 3.41

UBR11 = 0x000;

UMCTL1 = 0x04A;                     // Modulation

UCTL1 &= ~SWRST;                    // Initialize USART state machine

IE2 |= URXIE1;                      // Enable USART1 RX interrupts

}// end initUART1()

//------------------------------------------------------------------------------

void RX_TRF_mode(void) {   // Configure system for receive

//------------------------------------------------------------------------------

U0TCTL |= CKPH;                     // Set SPI Polarity __/--

P2OUT |= TRF_CS;                    // Turn on configuration mode

while(!(IFG1 & UTXIFG0));           // USART0 TX buffer ready?

TXBUF0 = ((RF-2400)<<1) | (AM_RX);

while(!(U0TCTL & TXEPT));           // Wait til TXreg is empty

P2OUT &= ~TRF_CS;                   // Turn off config mode

}// end RX_TRF_mode

//------------------------------------------------------------------------------

void RX_TRF(void) { // Receive data

//------------------------------------------------------------------------------

P1OUT |= RFR_RX_LED;                // Set RFR Recieve LED

U0TCTL &= ~CKPH;                    // Set SPI Polarity --\__

int i;

for(i = (PACKET_SIZE - 1); i >= 0; i--) {

TXBUF0 = 0x000;

while(!(IFG1 & UTXIFG0));       // Wait until TXBUF is empty

while(!(U0TCTL & TXEPT));       // Wait until TXreg is empty

recByte[i] = RXBUF0;            // Retrieve byte

}

P1OUT &= ~RFR_RX_LED;               // Clear RFR Recieve LED

}// end RX_TRF()

//------------------------------------------------------------------------------

void clkAddrBytes(unsigned int address_width) { // Clock in address bytes

//------------------------------------------------------------------------------

// When in TX mode, this function may be called to clock in address_width

// identical bytes of value ADDR_BYTE for the TX address.

unsigned int i;

for(i = 0; i < address_width; i += 1) {

while(!(IFG1 & UTXIFG0));           // USART0 TX buffer ready?

TXBUF0 = ADDR_BYTE;

}

}// end clkAddrBytes()

//------------------------------------------------------------------------------

void sendPCIA(void) {   // Send packet data to PCIA via RS-485

//------------------------------------------------------------------------------

for (int i = (PACKET_SIZE - 1); i >= 0; i--) {

wait(1000);

while (!(IFG2 & UTXIFG1));  // USART1 TX buffer ready?

TXBUF1 = recByte[i];        // Send byte i to PCIA

}

}// end sendPCIA()

//------------------------------------------------------------------------------

void wait(unsigned int wait_time) {   // Delay

//------------------------------------------------------------------------------

for (int i = 0; i < wait_time; i++);

}//end wait()

//------------------------------------------------------------------------------

#pragma vector=UART1RX_VECTOR

__interrupt void usart1_rx (void) {

// UART1RX Interupt Service Routine

//------------------------------------------------------------------------------

//unsigned int message = RXBUF1;              // Receive the message

switch(RXBUF1) {

case PING_PCIA_RFR:                 // if received a ping from PCIA

while (!(IFG2 & UTXIFG1));      // USART1 TX buffer ready?

TXBUF1 = PING_RFR_PCIA;         // Respond to ping

break;

case RESET_HND_REQUEST:             // if received a request to reset HAVE_NEW_DATA flag

HAVE_NEW_DATA = FALSE;          // reset HAVE_NEW_DATA flag

while (!(IFG2 & UTXIFG1));      // USART1 TX buffer ready?

TXBUF1 = RESET_HND_CONFIRM;     // Send reset data status confirmation

break;

case REQUEST_NEW_DATA:              // if received a request for new data

if (HAVE_NEW_DATA == TRUE) {    // If RFR has new data

while (!(IFG2 & UTXIFG1));  // USART1 TX buffer ready?

TXBUF1 = DATA_RFR_PCIA;     // Send data header

sendPCIA();                 // transmitt data to PCIA

HAVE_NEW_DATA = FALSE;      // reset HAVE_NEW_DATA flag

}

else {                          // If RFR has no new data

while (!(IFG2 & UTXIFG1));  // USART1 TX buffer ready?

TXBUF1 = NO_NEW_DATA;       // Tell the PCIA that this RFR has no new data

}

break;

default:

break;

}

}//end UART1RX ISR

## RFR: RFR_wireless_protocol.h

/******************************************************************************

File:   RFR_wireless_protocol.h

-----------------------------------------------------------------------------

Project        : Multi-channel Temperature Measurements with Telemetry

Author         : Casey T. Morrison, Dean R. Morrison

Created        : 03/04/2005

Last modified  : 04/11/2005

-----------------------------------------------------------------------------

Description : This is an include file for RFR_software.c that

defines constants and data structures for wireless

communication.

-----------------------------------------------------------------------------

Copyright :

The author retains all rights to this application.  Please do

not distribute this code in any form, shape or way.

*******************************************************************************/

//------------------------------------------------------------------------------

// TRF 2.4 GHz Modules

//------------------------------------------------------------------------------

#define   TRF_DR2     0x02                      // Data ready 2 (P2.1)

#define   TRF_DATA    0x02                      // Data channel 1 P3.1

#define   TRF_DATA2   0x04                      // Data channel 2 P3.2

#define   TRF_CLK     0x08                      // Clk            P3.3

#define   TRF_CE      0x04                      // Chip enable    P2.2

#define   TRF_CS      0x08                      // Chip select    P2.3

#define   UART_TX1    0x40                      // UART1 TX       P3.6

#define   UART_RX1    0x80                      // UART1 RX       P3.7

// Shockburst parameters:

// 1. Address length

#define   ADDR_W      2                         // Number of bytes for RX addrs (5 bytes max)

// 2. Receive channel address

#define   ADDR_BYTE   0x01

#define   ADDR_RXa    ADDR_BYTE                 // RX addr

#define   ADDR_RXb    ADDR_BYTE

#define   ADDR_RXc    ADDR_BYTE

#define   ADDR_RXd    ADDR_BYTE

#define   ADDR_RXe    ADDR_BYTE

// 3. Transmit channel address

#define   ADDR_TXa    ADDR_BYTE                 // TX addr

#define   ADDR_TXb    ADDR_BYTE

#define   ADDR_TXc    ADDR_BYTE

#define   ADDR_TXd    ADDR_BYTE

#define   ADDR_TXe    ADDR_BYTE

// 4. CRC

#define   CRC_L       1                         // '0' = 8-bit CRC (not recommended)

// '1' = 16-bit CRC (highly recommended)

#define   CRC_EN      1                         // '0' = disabled (not recommended)

// '1' = enabled (highly recommended)

// 5. General device parameters

#define   RX2_EN      1                         // '0' = one ch. receive

// '1' = two ch. receive

#define   CM          1                         // '0' = Direct mode

// '1' = ShockBurst mode (recommended)

#define   RFDR_SB     0                         // '0' = 250kbps

// '1' = 1Mbps

#define   XO_F        3                         // 16MHz crystal built-in (default)

#define   RF_PWR      3                         // 0dBm (changeable for smaller output and current consumption)

// 6. Active modes

#define   AM_TX       0                         // Transmit

#define   AM_RX       1                         // Receive

// 7. Frequency channel

//   2400MHz <= RF <= 2524MHz

//   receive chan 1 = RF    <--- never send data to

//   receive chan 2 = RF+8  <--- interested in!!

#define   RF          2450

//#define   RF          2467

// 8. LED Ports

#define   RFR_RX_LED  0x001                     // Port 1.0 - RFR Recieve LED

//#define   RFR_ACT_LED 0x002                     // Port 1.1 - RFR Active LED

// Miscellaneous TCA definitions

#define DELAY_AMT     5000                      // Number of cycles in each delay loop

#define DELAY1        0                         // Number of delay loops for delay 1

#define DELAY2        1                         // Number of delay loops for delay 2

#define DELAY3        1                         // Number of delay loops for delay 3

## PCIA: PCIA_software.c

//******************************************************************************

//  File: PCIA_software.c

//  Authors: Dean Morrison, Casey Morrison

//  Date Created:  03/15/2005

//  Date Modified: 04/11/2005

//

//  Description: This program handles the communication between the PC and the

//               array of RF Repeaters.

//

//

//                 MSP430F149

//            +-----------------+

//            |                 |

//            |            P1.0 |-----> RFR MUX channel select A

//            |            P1.1 |-----> RFR MUX channel select B

//            |            P1.2 |-----> RFR MUX channel select C

//            |                 |

//            |    (UTXD0) P3.4 |-----> Serial-to-USB Adapter RXD

//            |    (URXD0) P3.5 |<----- Serial-to-USB Adapter TXD

//            |    (UTXD1) P3.6 |-----> RFR TX MUX channels

//            |    (URXD1) P3.7 |<----- RFR RX MUX channels

//

//

//******************************************************************************

#include  "msp430x14x.h"            // Standard MSP430 equations

#include  "kilnTemp_defs.h"         // System-wide definitions

#define LONG_WAIT_TIME  60000

#define SHORT_WAIT_TIME 10000

#define   UART_TX0    0x10                      // UART1 TX       P3.4

#define   UART_RX0    0x20                      // UART1 RX       P3.5

#define   UART_TX1    0x40                      // UART1 TX       P3.6

#define   UART_RX1    0x80                      // UART1 RX       P3.7

// Function Prototypes

void initSys(void);

void Set_DCO (void);

void configUART0 (void);

void configUART1 (void);

void pingRFRs (void);

void wait_for_response (unsigned int);

void long_wait_for_response (void);

void requestData (void);

void requestDataHelper (int);

void resetDataStatus (void);

void resetDataStatusHelper (int);

void sendUSB (void);

void delay(unsigned int delay_cycles, unsigned int delay_loops);

// Global variables

static int active_RFRs[8] = {FALSE,FALSE,FALSE,FALSE,FALSE,FALSE,FALSE,FALSE};

static int current_RFR = 0;

static int keep_waiting = TRUE;

static int long_wait = FALSE;

static int RFR_activity_check_period = 10000;   // # of packets sent to PC before checking which RFRs are active again

static int channel[8] = {RFR_0, RFR_1, RFR_2, RFR_3, RFR_4, RFR_5, RFR_6, RFR_7};

static unsigned int Byte[PACKET_SIZE];

static unsigned int RFR_sending_data;

static int current_byte = PACKET_SIZE - 1;

static int data_RX = FALSE;

static int received_new_data = FALSE;

static int reset_have_new_data = FALSE;

static int ping_second_time = TRUE;

//------------------------------------------------------------------------------

void main(void) {

//------------------------------------------------------------------------------

// Initialize the MSP430 system

initSys();

// Set up analog multiplexer control bits (Port 1)

P1OUT  = 0x00;                        // Clear P1.0-P1.2 --> start with RFR_0

P1DIR |= 0x07;                        // Configure P1.0-P1.2 for output

// Set up UART0, UART1

configUART0();

configUART1();

// Determine which RFRs are active

pingRFRs();

// Communicate data between RFRs and PC

unsigned int i;

for (;;) {

for (i = 0; i < RFR_activity_check_period; i++) {

// Poll receivers for new data

requestData();			// Requests data from each RFR untill valid data is received

if (received_new_data == TRUE) {

sendUSB();			// send RFR data to PC via USB

received_new_data = FALSE;	// reset received_new_data flag

resetDataStatus();              // reset have_new_data flag on all active RFRs

}

}

pingRFRs();				// Determine which RFRs are active

}

} // end main()

//------------------------------------------------------------------------------

void initSys(void) {     //Initialize MSP430 System

//------------------------------------------------------------------------------

WDTCTL = WDTPW+WDTHOLD;               // Stop watchdog timer

// Configure MCLK (~2.0MHz)

BCSCTL1 |= DIVA_3;                    // ACLK= LFXT1CLK/8

Set_DCO();                            // Set DCO

// Default configurations for I/O ports

P1SEL = 0x00;                         // configure P1 for I/O

P1OUT = 0x00;                         // Clear P1.x

P1DIR = 0xFF;                         // Configure P1 for output

P2SEL = 0x00;                         // configure P2 for I/O

P2OUT = 0x00;                         // Clear P2.x

P2DIR = 0xFF;                         // Configure P2 for output

P3SEL = 0x00;                         // configure P3 for I/O

P3OUT = 0x00;                         // Clear P3.x

P3DIR = 0xFF;                         // Configure P3 for output

P4SEL = 0x00;                         // configure P4 for I/O

P4OUT = 0x00;                         // Clear P4.x

P4DIR = 0xFF;                         // Configure P4 for output

P5SEL = 0x00;                         // configure P5 for I/O

P5OUT = 0x00;                         // Clear P5.x

P5DIR = 0xFF;                         // Configure P5 for output

P6SEL = 0x00;                         // configure P6 for I/O

P6OUT = 0x00;                         // Clear P6.x

P6DIR = 0xFF;                         // Configure P6 for output

_EINT();                              // Enable interrupts

}// end initSys()

//------------------------------------------------------------------------------

void Set_DCO (void) {                   // Set DCO to selected frequency

//------------------------------------------------------------------------------

#define DELTA 488                       // Target DCO = DELTA*(4096) ~= 2MHz

unsigned int Compare, Oldcapture = 0;

CCTL2 = CM_1 + CCIS_1 + CAP;            // CAP, ACLK

TACTL = TASSEL_2 + MC_2 + TACLR;        // SMCLK, cont-mode, clear

while (1) {

while (!(CCIFG & CCTL2));           // Wait until capture occured

CCTL2 &= ~CCIFG;                    // Capture occured, clear flag

Compare = CCR2;                     // Get current captured SMCLK

Compare = Compare - Oldcapture;     // SMCLK difference

Oldcapture = CCR2;                  // Save current captured SMCLK

if (DELTA == Compare) break;        // If equal, leave "while(1)"

else if (DELTA < Compare) {

DCOCTL--;

if (DCOCTL == 0xFF) {           // DCO is too fast, slow it down

if (!(BCSCTL1 == (XT2OFF + DIVA_3)))

BCSCTL1--;              // Did DCO role under?, Sel lower RSEL

}

}

else {

DCOCTL++;                       // DCO is too slow, speed it down

if (DCOCTL == 0x00) {

if (!(BCSCTL1 == (XT2OFF + DIVA_3 + 0x07)))

BCSCTL1++;              // Did DCO role over? Sel higher RSEL

}

}

}

CCTL2 = 0;                              // Stop CCR2

TACTL = 0;                              // Stop Timer_A

}// end Set_DCO()

//------------------------------------------------------------------------------

void delay(unsigned int delay_cycles, unsigned int delay_loops) {

//------------------------------------------------------------------------------

unsigned int i;

unsigned int j;

for(i = 0; i < delay_loops; i++) {

for(j = 0; j < delay_cycles; j++) {

// do nothing

}

}

}

//------------------------------------------------------------------------------

void configUART0(void) {     //Initialize MSP430 System

//------------------------------------------------------------------------------

/*

Description: UART port for communication with external module

(RS-485 or FTDI) and configure for 9600 baud.

Application 1: MSP430-to-FTDI (dlp-usb232m14) communication

---------------+                      +---------

P3.4/UTXD0(32)|--------------------->|RXD

MSP430    P3.5/URXD0(33)|<---------------------|TXD        FTDI

|                      |

~RST/NMI|<---------------------|RESETO#

---------------+                      +---------

Application 2: MSP430 - RS485 communication

---------------+                      +---------

P3.4/UTXD0(32)|--------------------->|DI

MSP430    P3.5/URXD0(33)|<---------------------|RO         RS485

|                      |

---------------+                      +---------

*/

// Set up UART0

P3SEL |= 0x30;                        // P3.4,5 = USART0 TXD/RXD

ME1 |= UTXE0;                         // Enable USART0 TXD

UCTL0 |= CHAR;                        // 8-bit character, SWRST = 1

UTCTL0 |= SSEL1 + SSEL0 + URXSE;      // UCLK = SMCLK, start edge detect

UBR00 = 0xD0;                         // 9600 from 2Mhz

UBR10 = 0x00;

UMCTL0 = 0x00;                        // No modulation

UCTL0 &= ~SWRST;                      // Initialize USART state machine

}// end configUART1()

//------------------------------------------------------------------------------

void configUART1(void) {

//------------------------------------------------------------------------------

P3SEL |= UART_RX1 + UART_TX1;       // P3.6, P3.7 = USART1 RXD/TXD

ME2 |= 0x30;

UCTL1 |= CHAR;                      // 8-bit characters

UTCTL1 = SSEL0;                     // UCLK = ACLK

UBR01 = 0x003;                      // 32k/9600 - 3.41

UBR11 = 0x000;

UMCTL1 = 0x04A;                     // Modulation

UCTL1 &= ~SWRST;                    // Initialize USART state machine

//IE2 |= URXIE1;                      // Enable USART1 RX/TX interrupts

}// end configUART1()

//------------------------------------------------------------------------------

void clearBytes(void) {

//------------------------------------------------------------------------------

unsigned int i;

RFR_sending_data = 0;

for(i = 0; i < PACKET_SIZE; i++) {

Byte[i] = 0;

}

}

//------------------------------------------------------------------------------

void pingRFRs(void) {

// Determine which RFRs are active by sending a message to all of them one at a

// time, and waiting for a response

//------------------------------------------------------------------------------

IE2 |= URXIE1;                        // Enable USART1 RX interrupt

// DEBUG TEST

current_RFR = 0;

active_RFRs[current_RFR] = FALSE;     // set current RFR as inactive

ping_second_time = TRUE;

keep_waiting = TRUE;

P1OUT = channel[current_RFR];         // select the correct TX MUX channel

while (!(IFG2 & UTXIFG1));            // USART1 TX buffer ready?

TXBUF1 = PING_PCIA_RFR;               // Ping RFR[i]

wait_for_response(SHORT_WAIT_TIME);

if(ping_second_time == TRUE) {

while (!(IFG2 & UTXIFG1));        // USART1 TX buffer ready?

TXBUF1 = PING_PCIA_RFR;           // Ping RFR[i] one more time

wait_for_response(SHORT_WAIT_TIME);

}

for (current_RFR = 1; current_RFR < 8; current_RFR++) {

active_RFRs[current_RFR] = FALSE;     // set current RFR as inactive

ping_second_time = TRUE;

keep_waiting = TRUE;

P1OUT = channel[current_RFR];         // select the correct TX MUX channel

while (!(IFG2 & UTXIFG1));            // USART1 TX buffer ready?

TXBUF1 = PING_PCIA_RFR;               // Ping RFR[i]

wait_for_response(SHORT_WAIT_TIME);

if(ping_second_time == TRUE) {

while (!(IFG2 & UTXIFG1));        // USART1 TX buffer ready?

TXBUF1 = PING_PCIA_RFR;           // Ping RFR[i] one more time

wait_for_response(SHORT_WAIT_TIME);

}

}

IE2 &= URXID1;                            // Disable USART1 RX interrupt

} // END pingRFRs(void)

//------------------------------------------------------------------------------

void wait_for_response(unsigned int wait_time) {

// Wait for RX

// Note: wait_time is not in seconds

//------------------------------------------------------------------------------

unsigned int i;

for (i = 0; i < wait_time; i++) {

if (keep_waiting == FALSE) break;

}

if (long_wait == TRUE) long_wait_for_response();

} // END wait_for_response(int)

//------------------------------------------------------------------------------

void long_wait_for_response(void) {

// Wait for all RFR data bytes to be received

// Note: wait_time is not in seconds

//------------------------------------------------------------------------------

unsigned int i;

for (i = 0; i < LONG_WAIT_TIME; i++) {

if (keep_waiting == FALSE) break;

}

long_wait = FALSE;

} // END long_wait_for_response(void)

//------------------------------------------------------------------------------

void requestData(void) {

// Requests data from each RFR until valid data is received

//------------------------------------------------------------------------------

received_new_data = FALSE;

for (current_RFR = 0; current_RFR < 8; current_RFR++) { // Request data from RFR[0], then RFR[1], etc.

if (active_RFRs[current_RFR] == TRUE) { // If RFR[i] is active then request data from it

requestDataHelper(current_RFR);     // Request data from RFR[i]

}

if (received_new_data == TRUE) break;

}

} // END requestData(void)

//------------------------------------------------------------------------------

void requestDataHelper(int RFR_id) {

// requestData() Helper Function: Requests data from RFR # RFR_id

//------------------------------------------------------------------------------

keep_waiting = TRUE;

data_RX = FALSE;                      // not yet receiving data

P1OUT = channel[RFR_id];              // select the correct TX MUX channel

while (!(IFG2 & UTXIFG1));            // USART1 TX buffer ready?

IE2 |= URXIE1;                        // Enable USART1 RX interrupt

TXBUF1 = REQUEST_NEW_DATA;            // Request new data from RFR[RFR_id]

wait_for_response(SHORT_WAIT_TIME);

if (received_new_data == FALSE) {     // if no new data has been received, request again

while (!(IFG2 & UTXIFG1));        // USART1 TX buffer ready?

TXBUF1 = REQUEST_NEW_DATA;        // Request new data from RFR[RFR_id] again

wait_for_response(SHORT_WAIT_TIME);

}

IE2 &= URXID1;                        // Disable USART1 RX interrupt

data_RX = FALSE;                      // data reception done

} // END requestDataHelper(int)

//------------------------------------------------------------------------------

void resetDataStatus(void) {

// Resets the has_new_data flag on all active RFRs

//------------------------------------------------------------------------------

unsigned int i;

for (i = 0; i < 8; i++) {             // Send message to RFR[0], then RFR[1], etc.

if (active_RFRs[i] == TRUE) {     // If RFR[i] is active, then send message

resetDataStatusHelper(i);     // Tell RFR[i] to reset its has_new_data flag

}

}

} // END resetDataStatus(void)

//------------------------------------------------------------------------------

void resetDataStatusHelper(int RFR_id) {

// resetDataStatus() Helper Function: Resets have_new_data flag on RFR[RFR_id]

//------------------------------------------------------------------------------

keep_waiting = TRUE;

reset_have_new_data = FALSE;

P1OUT = channel[RFR_id];                    // select the correct TX MUX channel

while (!(IFG2 & UTXIFG1));                  // USART1 TX buffer ready?

IE2 |= URXIE1;                              // Enable USART1 RX interrupt

TXBUF1 = RESET_HND_REQUEST;                 // Request have_new_data flag of RFR[RFR_id] to

//be reset

wait_for_response(SHORT_WAIT_TIME);

//if (reset_have_new_data == FALSE) {         // if no confirmation received, request again

//    while (!(IFG2 & UTXIFG1));              // USART1 TX buffer ready?

//    TXBUF1 = RESET_HND_REQUEST;             // Request have_new_data flag of RFR[RFR_id] to

//                                            //be reset

//    wait_for_response(SHORT_WAIT_TIME);

//}

IE2 &= URXID1;                        // Disable USART1 RX interrupt

} // END requestDataHelper(int)

//------------------------------------------------------------------------------

void sendUSB (void) {

//------------------------------------------------------------------------------

// Transmit packet byte-by-byte

int i;

while(!(IFG1 & UTXIFG0));           // USART0 TX buffer ready?

TXBUF0 = RFR_sending_data;          // Tell PC which RFR sent data

for (i = (PACKET_SIZE - 1); i >= 0; i -= 1) {

while(!(IFG1 & UTXIFG0));       // USART0 TX buffer ready?

TXBUF0 = Byte[i];

}

}// end sendUSB()

//------------------------------------------------------------------------------

#pragma vector=UART1RX_VECTOR

__interrupt void usart1_rx (void) {

// UART1RX Interupt Service Routine

//------------------------------------------------------------------------------

if (data_RX == TRUE) {                  // if receiving data

Byte[current_byte] = RXBUF1;

if (current_byte == 0) {            // if on the last byte of transmission

data_RX = FALSE;                // data reception done

received_new_data = TRUE;

current_byte = (PACKET_SIZE - 1);     // reset current_byte

keep_waiting = FALSE;

long_wait = FALSE;

}

else current_byte = current_byte - 1;                // move to next byte

}

else {                                  // if receiving special byte

switch(RXBUF1) {

case PING_RFR_PCIA:             // if received a response to a ping

active_RFRs[current_RFR] = TRUE;  // set current RFR as active

ping_second_time = FALSE;

keep_waiting = FALSE;

//long_wait = FALSE;

break;

case DATA_RFR_PCIA:             // if received a New Data Header

data_RX = TRUE;             // begin data reception

current_byte = PACKET_SIZE - 1;

RFR_sending_data = current_RFR;

keep_waiting = TRUE;

long_wait = TRUE;

break;

case NO_NEW_DATA:               // if received a "No New Data" response

keep_waiting = FALSE;

data_RX = FALSE;

received_new_data = FALSE;

break;

case RESET_HND_CONFIRM:         // If recevie a confirmation of reseting the have_new_data flag from the RFR

reset_have_new_data = TRUE;

keep_waiting = FALSE;

break;

default:

received_new_data = FALSE;

break;

}

}

}

## USB: PCIA_main.c

//******************************************************************************

//  File: PCIA_main.c

//  Authors: Casey T. Morrison, Dean R. Morrison

//  Date Created:   03/08/2005

//  Date modified:  04/11/2005

//

//  Description: This program reads data on the USB port and interprets that

//               data according to the wireless protocol described in

//               USB_LE_host.h. Data is written to the file data.txt in the

//               "System Files" directory.

//******************************************************************************

#include <stdio.h>

#include <windows.h>

#include <time.h>

#include <string.h>

#include "FTD2XX.H"

#include "USB_LE_host.h"

#define	REFRESH_NUMBER	1

#define BAUD_RATE		9600	// Note: changing this value does NOT alter baud rate

// Function prototypes

void receiveBytes(void);

void printFileLabels(void);

void printScreenLabels(void);

void printPacketFile(void);

void printPacketScreen(unsigned int packet_number);

void printBytesFile(void);

void printBytesScreen(void);

// Global variables

unsigned int RFR_sending_data;

unsigned int recByte[PACKET_SIZE];

unsigned int status_batt;

unsigned int status_count;

unsigned int status_TC;

unsigned int status_sys;

char* TC_type;

char* sys_stat;

int continue_capture = TRUE;

int continue_recover = TRUE;

int devicePresent = FALSE;

int printData = TRUE;

DWORD numDevs = 0;

DWORD BytesReceived;

DWORD chars_RX_q;

DWORD chars_TX_q;

DWORD event_status;

FILE* data1;

FILE* data2;

FT_HANDLE pHandle = 0;

FT_STATUS status = -1;

// File names (choose one of the two file directory strings)

//const char fileDirectory[200] = "//Dean/SharedDocs/Senior Design Project/Temperature "

//                                "Measurement with Telemetry/Software/PC/System Files/";

const char fileDirectory[100] = "";

char file1Name[200] = "";

char file2Name[200] = "";

const char * dataChar = "8 data bits, 1 stop bit, no parity";

//------------------------------------------------------------------------------

void main() {

//------------------------------------------------------------------------------

int i = 0;		// Number of packets received between file openings

int j = 0;		// Cumulative packet number

int dummy1 = 0;	// dummy index1

int dummy2 = 0;	// dummy index2

// Construct files of the form: "data - Sat Apr 09 2005 11_50_10.txt"

//                              and "data.txt"

char file1String_a[200],

file1String_b[200],

file2String_a[200],

file2String_b[200],

file2String_c[200],

file2String_d[200];

struct tm *ptr;

time_t tm;

char tmpbuf[60];

tm = time(NULL);

ptr = localtime(&tm);

strftime(tmpbuf ,100 , "%a %b %d %Y %H_%M",ptr);

strcpy(file1String_a, fileDirectory);

strcpy(file1String_b, "data.txt");

strcat(file1String_a, file1String_b);

strcpy(file1Name, file1String_a);

strcpy(file2String_a, fileDirectory);

strcpy(file2String_b, "data - ");

strcpy(file2String_c, tmpbuf);

strcpy(file2String_d, ".txt");

strcat(file2String_a, file2String_b);

strcat(file2String_a, file2String_c);

strcat(file2String_a, file2String_d);

strcpy(file2Name, file2String_a);

// Initialize the system

printf("Interface Application for kilnTemp temperature capture software.\n\n");

printf("Writing data to files: \"%s\" and \"%s\"\n\n", file1Name, file2Name);

printf("System initialization...\n");

// Detect device on bus

status = FT_ListDevices(&numDevs,NULL,FT_LIST_NUMBER_ONLY);

if (status == FT_OK) {

printf("- Number devices present on the bus is: %d\n", numDevs);

}

else {

printf("* Error occured while trying to list the devices on the bus. "

"Error code: %d\n", status);

}

if (numDevs == 0) {

printf("* No devices found on the bus. Please insert a device or enter "

"Ctrl-C to quit.\n");

while(numDevs == 0) {

status = FT_ListDevices(&numDevs,NULL,FT_LIST_NUMBER_ONLY);

}

}

if (numDevs != 0) {

// Open the device

status = FT_Open(0, &pHandle);

if (status == FT_OK) {

printf("- Device status is: %d\n", status);

}

else {

printf("* Error occured while trying to open the device. "

"Error code: %d\n", status);

}

// Purge old data

status = FT_Purge(pHandle, FT_PURGE_RX);

if(status == FT_OK) {

printf("- System purged of old data.\n");

}

else {

printf("* Error occured while trying to purge system of old data. "

"Error code: %d\n", status);

}

// Set Baud rate

status = FT_SetBaudRate(pHandle, FT_BAUD_9600);

if(status == FT_OK) {

printf("- Baud rate set to %d.\n", BAUD_RATE);

}

else {

printf("* Error occured while trying to purge system of old data. "

"Error code: %d\n", status);

}

// Set data characteristics

status = FT_SetDataCharacteristics(pHandle, FT_BITS_8, FT_STOP_BITS_1, FT_PARITY_NONE);

if(status == FT_OK) {

printf("- Data characteristics set to: %s.\n", dataChar);

}

else {

printf("* Error occured while trying to purge system of old data. "

"Error code: %d\n", status);

}

// Open file for appending

data1 = fopen(file1Name, "w");

data2 = fopen(file2Name, "w");

// Print data packet column labels

printFileLabels();

printScreenLabels();

fclose(data1);

fclose(data2);

data1 = fopen(file1Name, "a");

data2 = fopen(file2Name, "a");

printf("Begin receiving data...\n");

// Continuously receive data

while (continue_capture == TRUE) {

for(i = 0; i < REFRESH_NUMBER; i++) {

printData = TRUE;

// Acquire data packet

receiveBytes();

// Check the status of the device

status = FT_GetStatus(pHandle, &chars_RX_q, &chars_TX_q, &event_status);

if(status == FT_OK) {

// do nothing

}

else {

printf("* Error occured while checking the device status. "

" Error code: %d\n", status);

continue_capture = FALSE;

printData = FALSE;

// Close the device

status = FT_Close(pHandle);

if (status == FT_OK) {

printf("- Device closed.\n");

}

else {

printf("* Error occured while trying to close the"

" device. Error code: %d\n", status);

}

}

// Try to recover device

while(continue_capture == FALSE) {

// Wait before trying to recover

for(dummy1 = 0; dummy1 < 1000; dummy1++) {

for(dummy2 = 0; dummy2 < 10000; dummy2++) {

// wait

}

}

printf("\n\nAttempting to recover USB device...\n");

continue_recover = TRUE;

// Detect device on bus

status = FT_ListDevices(&numDevs,NULL,FT_LIST_NUMBER_ONLY);

if (status == FT_OK) {

printf("- Number devices present on the bus is: "

"%d\n", numDevs);

}

else {

printf("* Error occured while trying to list the "

"devices on the bus. Error code: %d\n", status);

}

if (numDevs == 0) {

printf("* No devices found on the bus. "

"Please insert a device or enter "

"Ctrl-C to quit.\n");

while(numDevs == 0) {

status = FT_ListDevices(&numDevs,NULL,FT_LIST_NUMBER_ONLY);

}

}

// Device is plugged in, try to open the device

status = FT_Open(0, &pHandle);

if (status == FT_OK) {

printf("- Device status is: %d\n", status);

continue_capture = TRUE;

continue_recover = TRUE;

}

else {

printf("* Error occured while trying to open the "

"device. Error code: %d\n", status);

continue_recover = FALSE;

}

if(continue_recover == TRUE) {

// Purge old data

status = FT_Purge(pHandle, FT_PURGE_RX);

if(status == FT_OK) {

printf("- System purged of old data.\n");

}

else {

printf("* Error occured while trying to "

"purge system of old data. Error "

"code: %d\n", status);

}

// Set Baud rate

status = FT_SetBaudRate(pHandle, FT_BAUD_9600);

if(status == FT_OK) {

printf("- Baud rate set to %d.\n", BAUD_RATE);

}

else {

printf("* Error occured while trying to "

"set Baud rate. Error code: %d\n", status);

}

// Set data characteristics

status = FT_SetDataCharacteristics(pHandle, FT_BITS_8, FT_STOP_BITS_1, FT_PARITY_NONE);

if(status == FT_OK) {

printf("- Data characteristics set to: "

"%s.\n\n", dataChar);

printf("Continuing data capture...\n");

}

else {

printf("* Error occured while trying to "

"set data characteristics. Error "

"code: %d\n", status);

}

}

}

// Print data packet

if(printData == TRUE) {

printPacketFile();

printPacketScreen(j++);

}

}

// Close and reopen the file every REFRESH_NUMBER packets

fclose(data1);

fclose(data2);

data1 = fopen(file1Name, "a");

data2 = fopen(file2Name, "a");

}

// Close connection

FT_Close(pHandle);

}

return;

}

//------------------------------------------------------------------------------

void receiveBytes(void) {	// Capture all 27 bytes in a packet

//------------------------------------------------------------------------------

int i;

FT_Read(pHandle, &RFR_sending_data, 1, &BytesReceived);

for(i = PACKET_SIZE - 1; i >= 0; i -= 1) {

FT_Read(pHandle, &recByte[i], 1, &BytesReceived);

}

RX_packet.bytes.Byte_26 = recByte[26];

RX_packet.bytes.Byte_25 = recByte[25];

RX_packet.bytes.Byte_24 = recByte[24];

RX_packet.bytes.Byte_23 = recByte[23];

RX_packet.bytes.Byte_22 = recByte[22];

RX_packet.bytes.Byte_21 = recByte[21];

RX_packet.bytes.Byte_20 = recByte[20];

RX_packet.bytes.Byte_19 = recByte[19];

RX_packet.bytes.Byte_18 = recByte[18];

RX_packet.bytes.Byte_17 = recByte[17];

RX_packet.bytes.Byte_16 = recByte[16];

RX_packet.bytes.Byte_15 = recByte[15];

RX_packet.bytes.Byte_14 = recByte[14];

RX_packet.bytes.Byte_13 = recByte[13];

RX_packet.bytes.Byte_12 = recByte[12];

RX_packet.bytes.Byte_11 = recByte[11];

RX_packet.bytes.Byte_10 = recByte[10];

RX_packet.bytes.Byte_9  = recByte[9];

RX_packet.bytes.Byte_8  = recByte[8];

RX_packet.bytes.Byte_7  = recByte[7];

RX_packet.bytes.Byte_6  = recByte[6];

RX_packet.bytes.Byte_5  = recByte[5];

RX_packet.bytes.Byte_4  = recByte[4];

RX_packet.bytes.Byte_3  = recByte[3];

RX_packet.bytes.Byte_2  = recByte[2];

RX_packet.bytes.Byte_1  = recByte[1];

RX_packet.bytes.Byte_0  = recByte[0];

status_batt	 = (RX_packet.data.status >> 11) & 0x01;

status_count = (RX_packet.data.status >> 4 ) & 0x7F;

status_TC    = (RX_packet.data.status >> 1 ) & 0x07;

status_sys   = (RX_packet.data.status      ) & 0x01;

// Determine system status

switch (status_sys) {

case 0:

sys_stat = "OK";

break;

case 1:

sys_stat = "SW ERR";

break;

default:

sys_stat = "UNDET";

break;

}

// Determine TC type

switch (status_TC) {

case 0:

TC_type = "UNDET";

case 1:

TC_type = "B";

break;

case 2:

TC_type = "C";

break;

case 3:

TC_type = "J";

break;

case 4:

TC_type = "K";

break;

case 5:

TC_type = "R";

break;

case 6:

TC_type = "S";

break;

case 7:

TC_type = "T";

break;

default:

TC_type = "UNDET";

break;

}

}

//------------------------------------------------------------------------------

void printFileLabels(void) {	// Print data labels in data.txt file

//------------------------------------------------------------------------------

fprintf(data1, "\n");

fprintf(data1, "Batt Count TC Sys Temp TC0  TC1  TC2  TC3  TC4  TC5  TC6  TC7  TC8  ");

fprintf(data1, "TC9  TC10 TC11 TC12 TC13 TC14 TC15");

fprintf(data1, "\n\n");

fprintf(data1, "-    -     -  -   -    -    -    -    -    -    -    -    -    -    ");

fprintf(data1, "-    -    -    -    -    -    -\n");

fprintf(data2, "\n");

fprintf(data2, "Batt Count TC Sys Temp TC0  TC1  TC2  TC3  TC4  TC5  TC6  TC7  TC8  ");

fprintf(data2, "TC9  TC10 TC11 TC12 TC13 TC14 TC15");

fprintf(data2, "\n\n");

fprintf(data2, "-    -     -  -   -    -    -    -    -    -    -    -    -    -    ");

fprintf(data2, "-    -    -    -    -    -    -\n");

}

//------------------------------------------------------------------------------

void printScreenLabels(void) {	// Print data labels to the screen

//------------------------------------------------------------------------------

/*

printf("\n");

printf("Packet# Count TC_type Sys Temp TC0  TC1  TC2  TC3  TC4  TC5  TC6  TC7  TC8  ");

printf("TC9  TC10 TC11 TC12 TC13 TC14 TC15");

printf("\n\n");

*/

printf("\n\n");

}

//------------------------------------------------------------------------------

void printPacketFile(void) {	// Print data to data.txt file

//------------------------------------------------------------------------------

fprintf(data1, "%01d    ",	status_batt);

fprintf(data1, "%03d   ",	status_count);

fprintf(data1, "%01d  ",		status_TC);

fprintf(data1, "%01d   ",	status_sys);

fprintf(data1, "%04d ",		RX_packet.data.temp);

fprintf(data1, "%04d ",		RX_packet.data.TC_0);

fprintf(data1, "%04d ",		RX_packet.data.TC_1);

fprintf(data1, "%04d ",		RX_packet.data.TC_2);

fprintf(data1, "%04d ",		RX_packet.data.TC_3);

fprintf(data1, "%04d ",		RX_packet.data.TC_4);

fprintf(data1, "%04d ",		RX_packet.data.TC_5);

fprintf(data1, "%04d ",		RX_packet.data.TC_6);

fprintf(data1, "%04d ",		RX_packet.data.TC_7);

fprintf(data1, "%04d ",		RX_packet.data.TC_8);

fprintf(data1, "%04d ",		RX_packet.data.TC_9);

fprintf(data1, "%04d ",		RX_packet.data.TC_10);

fprintf(data1, "%04d ",		RX_packet.data.TC_11);

fprintf(data1, "%04d ",		RX_packet.data.TC_12);

fprintf(data1, "%04d ",		RX_packet.data.TC_13);

fprintf(data1, "%04d ",		RX_packet.data.TC_14);

fprintf(data1, "%04d",		RX_packet.data.TC_15);

fprintf(data1, "\n");

fprintf(data2, "%01d    ",	status_batt);

fprintf(data2, "%03d   ",	status_count);

fprintf(data2, "%01d  ",		status_TC);

fprintf(data2, "%01d   ",	status_sys);

fprintf(data2, "%04d ",		RX_packet.data.temp);

fprintf(data2, "%04d ",		RX_packet.data.TC_0);

fprintf(data2, "%04d ",		RX_packet.data.TC_1);

fprintf(data2, "%04d ",		RX_packet.data.TC_2);

fprintf(data2, "%04d ",		RX_packet.data.TC_3);

fprintf(data2, "%04d ",		RX_packet.data.TC_4);

fprintf(data2, "%04d ",		RX_packet.data.TC_5);

fprintf(data2, "%04d ",		RX_packet.data.TC_6);

fprintf(data2, "%04d ",		RX_packet.data.TC_7);

fprintf(data2, "%04d ",		RX_packet.data.TC_8);

fprintf(data2, "%04d ",		RX_packet.data.TC_9);

fprintf(data2, "%04d ",		RX_packet.data.TC_10);

fprintf(data2, "%04d ",		RX_packet.data.TC_11);

fprintf(data2, "%04d ",		RX_packet.data.TC_12);

fprintf(data2, "%04d ",		RX_packet.data.TC_13);

fprintf(data2, "%04d ",		RX_packet.data.TC_14);

fprintf(data2, "%04d",		RX_packet.data.TC_15);

fprintf(data2, "\n");

}

//------------------------------------------------------------------------------

void printPacketScreen(unsigned int packet_number) {	// Print data to screen

//------------------------------------------------------------------------------

printf("Packet #:  %-6d\n", packet_number);

printf("TCA count: %-6d                             ", status_count);

printf("Amplified, digitized thermocouple voltages\n");

printf("From RFR#: %-6d +---------------------------", RFR_sending_data);

printf("----------------------------------------------------------------------+\n");

printf("TC type:   %-6s | TC_0  TC_1  TC_2  TC_3  TC_4  TC_5  TC_6  TC_7  ", TC_type);

printf("TC_8  TC_9  TC_10 TC_11 TC_12 TC_13 TC_14 TC_15 |\n");

printf("Sys stat:  %-6s | %04d  ", sys_stat, RX_packet.data.TC_0);

printf("%04d  ",	RX_packet.data.TC_1);

printf("%04d  ",	RX_packet.data.TC_2);

printf("%04d  ",	RX_packet.data.TC_3);

printf("%04d  ",	RX_packet.data.TC_4);

printf("%04d  ",	RX_packet.data.TC_5);

printf("%04d  ",	RX_packet.data.TC_6);

printf("%04d  ",	RX_packet.data.TC_7);

printf("%04d  ",	RX_packet.data.TC_8);

printf("%04d  ",	RX_packet.data.TC_9);

printf("%04d  ",	RX_packet.data.TC_10);

printf("%04d  ",	RX_packet.data.TC_11);

printf("%04d  ",	RX_packet.data.TC_12);

printf("%04d  ",	RX_packet.data.TC_13);

printf("%04d  ",	RX_packet.data.TC_14);

printf("%04d  |\n",	RX_packet.data.TC_15);

printf("Amb. Temp: %-6d +--------------------------------", RX_packet.data.temp);

printf("-----------------------------------------------------------------+\n\n");

/*

printf("%05d   ",	packet_number);

printf("%03d   ",	status_count);

printf("%-6s  ",	TC_type);

printf("%01d   ",	status_sys);

printf("%04d ",		RX_packet.data.temp);

printf("%04d ",		RX_packet.data.TC_0);

printf("%04d ",		RX_packet.data.TC_1);

printf("%04d ",		RX_packet.data.TC_2);

printf("%04d ",		RX_packet.data.TC_3);

printf("%04d ",		RX_packet.data.TC_4);

printf("%04d ",		RX_packet.data.TC_5);

printf("%04d ",		RX_packet.data.TC_6);

printf("%04d ",		RX_packet.data.TC_7);

printf("%04d ",		RX_packet.data.TC_8);

printf("%04d ",		RX_packet.data.TC_9);

printf("%04d ",		RX_packet.data.TC_10);

printf("%04d ",		RX_packet.data.TC_11);

printf("%04d ",		RX_packet.data.TC_12);

printf("%04d ",		RX_packet.data.TC_13);

printf("%04d ",		RX_packet.data.TC_14);

printf("%04d",		RX_packet.data.TC_15);

printf("\n");

*/

/*

printf("Packet #:  %-6d          +0    +1    +2    +3\n", packet_number);

printf("TCA count: %-6d   TC_0   %04d  %04d  %04d  %04d\n", status_count, RX_packet.data.TC_0, RX_packet.data.TC_1, RX_packet.data.TC_2, RX_packet.data.TC_3);

printf("TC type:   %-6s   TC_4   %04d  %04d  %04d  %04d\n", TC_type, RX_packet.data.TC_4, RX_packet.data.TC_5, RX_packet.data.TC_6, RX_packet.data.TC_7);

printf("Sys stat:  %-6s   TC_8   %04d  %04d  %04d  %04d\n", sys_stat, RX_packet.data.TC_8, RX_packet.data.TC_9, RX_packet.data.TC_10, RX_packet.data.TC_11);

printf("Amb. Temp: %-6d   TC_12  %04d  %04d  %04d  %04d\n\n", RX_packet.data.temp, RX_packet.data.TC_12, RX_packet.data.TC_13, RX_packet.data.TC_14, RX_packet.data.TC_15);

*/

}

//------------------------------------------------------------------------------

void printBytesFile(void) {		// Print data in byte form to data.txt file

//------------------------------------------------------------------------------

fprintf(data1, "\n");

fprintf(data1, "Packet %03d bytes:\n", status_count);

fprintf(data1, "Byte_26: %02X\n", RX_packet.bytes.Byte_26);

fprintf(data1, "Byte_25: %02X\n", RX_packet.bytes.Byte_25);

fprintf(data1, "Byte_24: %02X\n", RX_packet.bytes.Byte_24);

fprintf(data1, "Byte_23: %02X\n", RX_packet.bytes.Byte_23);

fprintf(data1, "Byte_22: %02X\n", RX_packet.bytes.Byte_22);

fprintf(data1, "Byte_21: %02X\n", RX_packet.bytes.Byte_21);

fprintf(data1, "Byte_20: %02X\n", RX_packet.bytes.Byte_20);

fprintf(data1, "Byte_19: %02X\n", RX_packet.bytes.Byte_19);

fprintf(data1, "Byte_18: %02X\n", RX_packet.bytes.Byte_18);

fprintf(data1, "Byte_17: %02X\n", RX_packet.bytes.Byte_17);

fprintf(data1, "Byte_16: %02X\n", RX_packet.bytes.Byte_16);

fprintf(data1, "Byte_15: %02X\n", RX_packet.bytes.Byte_15);

fprintf(data1, "Byte_14: %02X\n", RX_packet.bytes.Byte_14);

fprintf(data1, "Byte_13: %02X\n", RX_packet.bytes.Byte_13);

fprintf(data1, "Byte_12: %02X\n", RX_packet.bytes.Byte_12);

fprintf(data1, "Byte_11: %02X\n", RX_packet.bytes.Byte_11);

fprintf(data1, "Byte_10: %02X\n", RX_packet.bytes.Byte_10);

fprintf(data1, "Byte_9:  %02X\n", RX_packet.bytes.Byte_9);

fprintf(data1, "Byte_8:  %02X\n", RX_packet.bytes.Byte_8);

fprintf(data1, "Byte_7:  %02X\n", RX_packet.bytes.Byte_7);

fprintf(data1, "Byte_6:  %02X\n", RX_packet.bytes.Byte_6);

fprintf(data1, "Byte_5:  %02X\n", RX_packet.bytes.Byte_5);

fprintf(data1, "Byte_4:  %02X\n", RX_packet.bytes.Byte_4);

fprintf(data1, "Byte_3:  %02X\n", RX_packet.bytes.Byte_3);

fprintf(data1, "Byte_2:  %02X\n", RX_packet.bytes.Byte_2);

fprintf(data1, "Byte_1:  %02X\n", RX_packet.bytes.Byte_1);

fprintf(data1, "Byte_0:  %02X\n", RX_packet.bytes.Byte_0);

fprintf(data1, "\n");

fprintf(data2, "\n");

fprintf(data2, "Packet %03d bytes:\n", status_count);

fprintf(data2, "Byte_26: %02X\n", RX_packet.bytes.Byte_26);

fprintf(data2, "Byte_25: %02X\n", RX_packet.bytes.Byte_25);

fprintf(data2, "Byte_24: %02X\n", RX_packet.bytes.Byte_24);

fprintf(data2, "Byte_23: %02X\n", RX_packet.bytes.Byte_23);

fprintf(data2, "Byte_22: %02X\n", RX_packet.bytes.Byte_22);

fprintf(data2, "Byte_21: %02X\n", RX_packet.bytes.Byte_21);

fprintf(data2, "Byte_20: %02X\n", RX_packet.bytes.Byte_20);

fprintf(data2, "Byte_19: %02X\n", RX_packet.bytes.Byte_19);

fprintf(data2, "Byte_18: %02X\n", RX_packet.bytes.Byte_18);

fprintf(data2, "Byte_17: %02X\n", RX_packet.bytes.Byte_17);

fprintf(data2, "Byte_16: %02X\n", RX_packet.bytes.Byte_16);

fprintf(data2, "Byte_15: %02X\n", RX_packet.bytes.Byte_15);

fprintf(data2, "Byte_14: %02X\n", RX_packet.bytes.Byte_14);

fprintf(data2, "Byte_13: %02X\n", RX_packet.bytes.Byte_13);

fprintf(data2, "Byte_12: %02X\n", RX_packet.bytes.Byte_12);

fprintf(data2, "Byte_11: %02X\n", RX_packet.bytes.Byte_11);

fprintf(data2, "Byte_10: %02X\n", RX_packet.bytes.Byte_10);

fprintf(data2, "Byte_9:  %02X\n", RX_packet.bytes.Byte_9);

fprintf(data2, "Byte_8:  %02X\n", RX_packet.bytes.Byte_8);

fprintf(data2, "Byte_7:  %02X\n", RX_packet.bytes.Byte_7);

fprintf(data2, "Byte_6:  %02X\n", RX_packet.bytes.Byte_6);

fprintf(data2, "Byte_5:  %02X\n", RX_packet.bytes.Byte_5);

fprintf(data2, "Byte_4:  %02X\n", RX_packet.bytes.Byte_4);

fprintf(data2, "Byte_3:  %02X\n", RX_packet.bytes.Byte_3);

fprintf(data2, "Byte_2:  %02X\n", RX_packet.bytes.Byte_2);

fprintf(data2, "Byte_1:  %02X\n", RX_packet.bytes.Byte_1);

fprintf(data2, "Byte_0:  %02X\n", RX_packet.bytes.Byte_0);

fprintf(data2, "\n");

}

//------------------------------------------------------------------------------

void printBytesScreen(void) {	// Print data in byte form to screen

//------------------------------------------------------------------------------

printf("\n");

printf("Packet %03d bytes:\n", status_count);

printf("Byte_26: %02X\n", RX_packet.bytes.Byte_26);

printf("Byte_25: %02X\n", RX_packet.bytes.Byte_25);

printf("Byte_24: %02X\n", RX_packet.bytes.Byte_24);

printf("Byte_23: %02X\n", RX_packet.bytes.Byte_23);

printf("Byte_22: %02X\n", RX_packet.bytes.Byte_22);

printf("Byte_21: %02X\n", RX_packet.bytes.Byte_21);

printf("Byte_20: %02X\n", RX_packet.bytes.Byte_20);

printf("Byte_19: %02X\n", RX_packet.bytes.Byte_19);

printf("Byte_18: %02X\n", RX_packet.bytes.Byte_18);

printf("Byte_17: %02X\n", RX_packet.bytes.Byte_17);

printf("Byte_16: %02X\n", RX_packet.bytes.Byte_16);

printf("Byte_15: %02X\n", RX_packet.bytes.Byte_15);

printf("Byte_14: %02X\n", RX_packet.bytes.Byte_14);

printf("Byte_13: %02X\n", RX_packet.bytes.Byte_13);

printf("Byte_12: %02X\n", RX_packet.bytes.Byte_12);

printf("Byte_11: %02X\n", RX_packet.bytes.Byte_11);

printf("Byte_10: %02X\n", RX_packet.bytes.Byte_10);

printf("Byte_9:  %02X\n", RX_packet.bytes.Byte_9);

printf("Byte_8:  %02X\n", RX_packet.bytes.Byte_8);

printf("Byte_7:  %02X\n", RX_packet.bytes.Byte_7);

printf("Byte_6:  %02X\n", RX_packet.bytes.Byte_6);

printf("Byte_5:  %02X\n", RX_packet.bytes.Byte_5);

printf("Byte_4:  %02X\n", RX_packet.bytes.Byte_4);

printf("Byte_3:  %02X\n", RX_packet.bytes.Byte_3);

printf("Byte_2:  %02X\n", RX_packet.bytes.Byte_2);

printf("Byte_1:  %02X\n", RX_packet.bytes.Byte_1);

printf("Byte_0:  %02X\n", RX_packet.bytes.Byte_0);

printf("\n");

}

## USB: USB_LE_host.h

//******************************************************************************

//  File: USB_LE_host.h

//  Authors: Casey Morrison, Dean Morrison

//  Date Created:   03/08/2005

//  Date Modified:  03/25/2005

//

//  Description: Include file for USB data acquisition that accommodates Little

//               Endian hosts

//******************************************************************************

// Constants

#define UNDET_TYPE  0x000

#define B_TYPE      0x001

#define C_TYPE      0x002

#define J_TYPE      0x003

#define K_TYPE      0x004

#define R_TYPE      0x005

#define S_TYPE      0x006

#define T_TYPE      0x007

#define SYS_OK      0

#define SYS_NOT_OK  1

#define BATT_OK     0

#define LOW_BATT    1

#define FALSE       0

#define TRUE        1

#define	PACKET_SIZE	27

// MSP430 Data Structures

struct sys_stat {

//                   11 10                           4 3            1 0

//              +------+------------------------------+--------------+-----+

//              | batt |            count             |      TC      | sys |

//              +------+------------------------------+--------------+-----+

unsigned int sys  : 1;

unsigned int TC   : 3;

unsigned int count: 7;

unsigned int batt : 1;

unsigned int      : 0;

};

struct packet_data {

//		 215        204 203        192 191        180 179  12 11           0

//		+--------------+--------------+--------------+-------+--------------+

//		|    status    |     temp     |     TC_0     |  ...  |     TC_15    |

//		+--------------+--------------+--------------+-------+--------------+

unsigned int TC_15  : 12;	// bits[0  : 11]

unsigned int TC_14  : 12;	// bits[12 : 23]

unsigned int        : 0;	// force alignment at next word boundary

unsigned int TC_13  : 12;	// bits[24 : 35]

unsigned int TC_12  : 12;	// bits[36 : 47]

unsigned int        : 0;	// force alignment at next word boundary

unsigned int TC_11  : 12;	// bits[48 : 59]

unsigned int TC_10  : 12;	// bits[60 : 71]

unsigned int        : 0;	// force alignment at next word boundary

unsigned int TC_9   : 12;	// bits[72 : 83]

unsigned int TC_8   : 12;	// bits[84 : 95]

unsigned int        : 0;	// force alignment at next word boundary

unsigned int TC_7   : 12;	// bits[96 :107]

unsigned int TC_6   : 12;	// bits[108:119]

unsigned int        : 0;	// force alignment at next word boundary

unsigned int TC_5   : 12;	// bits[120:131]

unsigned int TC_4   : 12;	// bits[132:143]

unsigned int        : 0;	// force alignment at next word boundary

unsigned int TC_3   : 12;	// bits[144:155]

unsigned int TC_2   : 12;	// bits[156:167]

unsigned int        : 0;	// force alignment at next word boundary

unsigned int TC_1   : 12;	// bits[168:179]

unsigned int TC_0   : 12;	// bits[180:191]

unsigned int        : 0;	// force alignment at next word boundary

unsigned int temp   : 12;	// bits[192:203]

unsigned int status : 12;	// bits[204:215]

};

struct packet_bytes {

//		 215   204 203   192 191   180 179   172 171  16 15      8 7       0

//		+---------+---------+---------+---------+-------+---------+---------+

//		| Byte_26 | Byte_25 | Byte_24 | Byte_23 |  ...  | Byte_1  | Byte_0  |

//		+---------+---------+---------+---------+-------+---------+---------+

//  unsigned int        : 0;

unsigned int Byte_0 : 8;	// bits[0  :  7]

unsigned int Byte_1 : 8;	// bits[8  : 15]

unsigned int Byte_2 : 8;	// bits[16 : 23]

unsigned int        : 0;	// force alignment at next word boundary

unsigned int Byte_3 : 8;	// bits[24 : 31]

unsigned int Byte_4 : 8;	// bits[32 : 39]

unsigned int Byte_5 : 8;	// bits[40 : 47]

unsigned int        : 0;	// force alignment at next word boundary

unsigned int Byte_6 : 8;	// bits[48 : 55]

unsigned int Byte_7 : 8;	// bits[56 : 63]

unsigned int Byte_8 : 8;	// bits[64 : 71]

unsigned int        : 0;	// force alignment at next word boundary

unsigned int Byte_9 : 8;	// bits[72 : 79]

unsigned int Byte_10: 8;	// bits[80 : 87]

unsigned int Byte_11: 8;	// bits[88 : 95]

unsigned int        : 0;	// force alignment at next word boundary

unsigned int Byte_12: 8;	// bits[96 :103]

unsigned int Byte_13: 8;	// bits[104:111]

unsigned int Byte_14: 8;	// bits[112:119]

unsigned int        : 0;	// force alignment at next word boundary

unsigned int Byte_15: 8;	// bits[120:127]

unsigned int Byte_16: 8;	// bits[128:135]

unsigned int Byte_17: 8;	// bits[136:143]

unsigned int        : 0;	// force alignment at next word boundary

unsigned int Byte_18: 8;	// bits[144:151]

unsigned int Byte_19: 8;	// bits[152:159]

unsigned int Byte_20: 8;	// bits[160:167]

unsigned int        : 0;	// force alignment at next word boundary

unsigned int Byte_21: 8;	// bits[168:175]

unsigned int Byte_22: 8;	// bits[176:183]

unsigned int Byte_23: 8;	// bits[184:191]

unsigned int        : 0;	// force alignment at next word boundary

unsigned int Byte_24: 8;	// bits[192:199]

unsigned int Byte_25: 8;	// bits[200:207]

unsigned int Byte_26: 8;	// bits[208:215]

};

union packet {

struct packet_data data;

struct packet_bytes bytes;

}TX_packet,RX_packet;

/*

TX_packet.data.TC_15------------------------------------------------------------+

TX_packet.data.TC_0--------------------------------------+                      |

TX_packet.data.temp-----------------------+              |                      |

TX_packet.data.status------+              |              |                      |

|              |              |                      |

215   |    204 203   |   192 191    |    180 179  12 11    |      0

+------v-------+------v-------+------v-------+-------+------v-------+

|    status    |     temp     |     TC_0     |  ...  |     TC_15    |

+---------+----+----+---------+---------+----+--+----+----+---------+

| Byte_26 | Byte_25 | Byte_24 | Byte_23 |  ...  | Byte_1  | Byte_0  |

+----^----+----^----+----^----+----^----+-------+----^----+----^----+

|         |         |         |                 |         |

TX_pscket.bytes.Byte_26--+         |         |         |                 |         |

TX_packet.bytes.Byte_25------------+         |         |                 |         |

TX_packet.bytes.Byte_24----------------------+         |                 |         |

TX_packet.bytes.Byte_23--------------------------------+                 |         |

TX_packet.bytes.Byte_1---------------------------------------------------+         |

TX_packet.bytes.Byte_0-------------------------------------------------------------+

*/

# Footnotes

RT = Ambient room temperature.

RT = Ambient room temperature in which the TCA is housed.