EEL 4914 Senior Design

Project Proposal

January 31, 2005

Multi-channel Temperature Measurement with Telemetry

Submitted by:

Casey Morrison

Dean Morrison

Table of Contents

Project Abstract	3

Introduction	3

Technical Objectives	3

Cost Objectives	4

Concept Screening Matrix	4

Study Organization	6

References	7

Materials and Resources	8

# Project Abstract

The goal of this project is to design and build a multi-channel temperature measurement device with wireless data transmission. This product is intended to be used for various industrial process-monitoring applications. Commissioned by Dr. Karl Gugel on behalf of Digital Control Lab, this device is originally intended for the cement and ceramics industries.

The challenge of this project is to create a low-power temperature sensing module that is capable of both accurate measurements and real-time data transmission. Although certain aspects of the design will be application-specific, the product as a whole could conceivably be reconfigured for a variety of environments.

# Introduction

The primary application of this product is for process-monitoring in the cement and ceramics industries. Secondary applications include virtually any type of industrial process-monitoring where real-time temperature data is necessary.

Most of the existing, similar products in the cement and ceramics industries do not employ telemetry and therefore are not real-time. Making temperature measurement real-time in these industries will significantly increase productivity and reduce waste. The combination of data logging with real-time measurements will help the industries recognize and predict trends in their process-monitoring and will aid in increasing efficiency.

# Technical Objectives

The preliminary requirements specifications for this design are presented in Table 1 below.

Table 1

# Cost Objectives

A prototype for this project is expected to cost anywhere from $170 to $207 (Table 2 details this cost calculation). This estimate includes only one RF receiver station, not multiple like the actual application would require.

Table 2

It is difficult to find products with the same characteristics and application environments. Honeywell International makes a line of Wireless Analog Input Transmitters that cost approximately $1190.00. Not only is the Honeywell product significantly more expensive than this project, but it is also unclear whether it can measure temperatures as high as 1400 °C, the upper measurement range of our project prototype.

# Concept Screening Matrix

The matrix used to select the design concepts that will be pursued during this project are shown below in Tables 3.1 – 3.4.

Table 3.1

Table 3.2

Table 3.3

Table 3.4

# Study Organization

The research, design, implementation, and testing for this project will be organized in the manner depicted in Table 4 and Figure 1. The high-level organization of this project can be described as starting with research and concept generation, followed by design and experimentation of the various functional segments, construction, and then testing and verification. The sequence and duration of the major tasks of this project are shown in Figure 1.

As shown in Table 4, the major tasks of this project will be generating the project idea, research, creating a concept generation matrix, thermocouple/analog circuit experimentation and design, MSP430 experimentation and design, transceiver experimentation and design, receiver-side design, PCB layout, PC interface and software development, assembly, testing and reconfiguration, documentation review, and demonstration. Major milestones of the project include the finalization of the project idea, completion of the system-level design and detailed design, completion of assembly, and completion of testing and verification.

Table 4

Figure 1

# References

Tables 5.1 and 5.2 list the various resources that have been, and continue to be, referenced during the development of this product.

| Reference | Description | Reference capacity | Link to resource |
| --- | --- | --- | --- |
| Thermocouple reference chart | Chart that differentiates between thermocouple type, temperature range, composition, color code, voltage range, etc. | Specifications and standards | http://www.omega.com/techref/colorcodes.html |
| Texas Instruments | Integrated Circuit (IC) manufacturer | Data sheets, product features, and pricing information for various ICs | http://www.ti.com/ |
| Analog Devices | Integrated Circuit (IC) manufacturer | Data sheets, product features, and pricing information for various amplifiers, voltage regulators, and DC-to-DC converters | http://www.analog.com |
| Spark Fun Electronics | Electronics distributor and development board manufacturer | Data sheets, product features, and pricing information for various transceivers and microcontrollers | www.sparkfun.com/ |
| Table 5.1 |
| Dr. Karl Gugel | Professor and owner of Digital Control Lab | Technical direction | gugel@ecel.ufl.edu |
| Tsang Wei Huang | Graduate student and Teaching Assistant | Technical support | twhuang@ufl.edu |
| Grzegorz Cieslewski | Graduate student, Teaching Assistant, Research Assistant | Technical support | grzegorz@ufl.edu |

Table 5.2

# Materials and Resources

Table 6 shows a general list of anticipated major components for this project, including the subassemblies in which they will reside.  Resources needed for this project include a 16-channel thermocouple simulator, PCB design software, and access to relevant industry testing environments.

| Functional Assemblies | Subassemblies | Components |
| --- | --- | --- |
| Transmit-side Assembly | Thermocouple/Analog Circuit | Thermocouples |
|  |  | DC/DC Boosters and regulators |
|  |  | Analog Multiplexer |
|  |  | Amplifier |
|  | Data Processing | A/D Converter |
|  |  | Microcontroller |
|  | Data Transmission | Transceiver |
| Receive-side Assembly | Data Receive | Transceiver |
|  | Data Processing | Microcontroller |
|  |  | RS232 Line Driver |
| PC Interface | PC Interface | RS232 Line Receiver |
|  |  | Microcontroller |
|  |  | Serial to USB interface |

Table 6