Project # 8

EEL 4914 Senior Design

System Level Design Report

February 21, 2005

Multi-channel Temperature Measurement with Telemetry

Submitted by:

Casey Morrison

Dean Morrison

Table of Contents

Project Abstract	3

Introduction	3

Technical Objectives	3

Cost Objectives	4

Concept Screening Matrix	5

System Level Presentation	6

System Diagrams	6

Subassembly Diagrams	7

Expected Outcome	9

Study Organization	9

References	10

Materials and Resources	11

# Project Abstract

The goal of this project is to design and build a multi-channel temperature measurement device with wireless data transmission. This product is intended to be used for various industrial process-monitoring applications. Commissioned by Dr. Karl Gugel on behalf of Digital Control Lab, this device is originally intended for the cement and ceramics industries.

The challenge of this project is to create a low-power temperature sensing module that is capable of both accurate measurements and real-time data transmission. Although certain aspects of the design will be application-specific, the product as a whole could be reconfigured for a variety of environments.

# Introduction

The primary application of this product is for process-monitoring in the cement and ceramics industries. Secondary applications include virtually any type of industrial process-monitoring where real-time temperature data is necessary.

Most of the existing, similar products in the cement and ceramics industries do not employ telemetry and therefore are not real-time. Making temperature measurement real-time in these industries will significantly increase productivity and reduce waste. The combination of data logging with real-time measurements will help the industries recognize and predict trends in their process-monitoring and will aid in increasing efficiency.

# Technical Objectives

The requirements specifications for this design are presented in Table 1 below.

| Requirement number | Parameter | Conditions | Value | Unit |
| --- | --- | --- | --- | --- |
|  |  |  | Min | Nominal | Max |  |
| 1 | Detectable temperature |  | 100 |  | 1400 | Celsius |
| 2 | Sampling rate |  | 1 |  | 3 | minutes per 16 samples |
| 3 | Transmit-side supply voltage |  | 2.4 |  | 4.8 | Volts |
| 4 | Transmit-side power consumption | Max load |  | 0.1 |  | Watts |
| 5 | Transmission frequency |  | 2.4 | 2.4 | 2.27 | GHz |
| 6 | Wireless transmission range |  |  | 10 | 20 | meters |
| 7 | Temperature resolution |  |  | 1 | 2 | Celsius |
| 8 | Electronics box width |  |  |  | 18 | cm |
| 9 | Electronics box height |  |  |  | 18 | cm |
| 10 | Electronics box length |  |  |  | 18 | cm |
| 11 | Ambient temperature inside electronics box |  |  |  | 200 | Celsius |
| 13 | Duration in kiln |  | 45 |  | 540 | minutes |

Table 1: Requirements Specification

# Cost Objectives

A prototype for this project is expected to cost anywhere from $585 to $1,108 (Table 2 details this cost calculation). This estimate includes only one RF receiver station, not multiple like the actual application would most likely require.

Table 2: Prototype Cost Projection

It is difficult to find products with the same characteristics and application environments. Honeywell International makes a line of Wireless Analog Input Transmitters that cost approximately $1190.00. The price of this product, however, does not include the temperature measuring device(s) necessary for its application. For the extreme temperature range that our product is designed for, temperature measurement devices are limited almost exclusively to R or S type thermocouples. As Table 2 shows, these thermocouples are relatively expensive and make up the majority of the cost of our product. So, an existing product like the one offered by Honeywell International would not only be significantly more expensive (after the purchase of the temperature measurement devices), but it is also unclear whether it provides the same functionality and features that our system will provide.

# Concept Screening Matrix

The matrix used to select the design concepts that will be pursued during this project are shown below in Tables 3.1 – 3.4.

Table 3.1: Concept Screening Matrix – Definition of Concept Variables

Table 3.2: Concept Screening Matrix – Concepts A through E

Table 3.3: Concept Screening Matrix – Concepts F through J

Table 3.4: Concept Screening Matrix – Concepts K, L, Reference

As the tables above show, Concept C ranks the highest among all of the proposed concepts.  Concept C is composed of a multi-channel analog to digital converter, an MSP430F149, four rechargeable 1.2V D batteries, and R-type thermocouples amplified by a 3.3V amplifier.  These components and design strategies combine to make up the most attractive design for our projects purpose.

# System Level Presentation

### System Diagrams

The product being designed is shown below (Figure 1) in a visualization of its operating environment.

Figure 1: Overall System Visualization

This system is made up of three assemblies: the Transmit-Side Assembly (TSA), the Receive-Side Assembly (RSA), and the PC-Side Assembly (PCSA).  The functional relationships between these assemblies are depicted in Figure 2.

Figure 2: Assembly Interactions

### Subassembly Diagrams

The Transmit-Side Assembly shown in Figure 2 has an internal functional structure that is depicted in Figure 3. The main purpose of the TSA is to receive analog voltages that represent temperature readings from the 16 thermocouples attached to it. These voltages will be amplified, packeted, and transmitted wirelessly via the onboard 2.4GHz transceiver. Among the data transmitted by the TSA will be the ambient temperature inside the heat-shielding box where the TSA is housed. This temperature will be measured by a temperature sensing IC on the TSA. The TSA will be powered by a 2.4V to 4.8V rechargeable battery source.

Figure 3: TSA Block Diagram

The Receive-Side Assembly shown in Figure 2 has an internal functional structure that is depicted in Figure 4. The main purpose of the RSA is to receive the temperature data that is wirelessly transmitted by the TSA and transmit it to the PCSA via an RS-485 serial interface. The RSA will be powered by a single 4.5V – 5.0V source that will be regulated to 3.3V.

Figure 4: RSA Block Diagram

Figure 5: PCSA Block Diagram

Each component will be prototyped and tested for functionality, timing, and/or accuracy. Once each subassembly design is verified via these tests, a custom printed circuit board (PCB) will be milled for each subassembly. These boards will undergo further testing with particular attention paid to boundary value testing, optimization, and stress testing.

If the components meet their respective minimum requirements, and the system as a whole meets its requirements (see Table 1), then the goal of producing a working prototype will be met. However, time permitting, further optimization and improvements may warrant the design and production of several versions of PCBs.

# Expected Outcome

The final outcome of this project will be a working prototype consisting of at least one of each of the subassemblies (TSA, RSA, and PCSA). The system will be configurable for different thermocouple types and thus different temperature measurement ranges. The one or more RSA(s) will communicate with the PCSA over long distances of RS485 wire. At the PC base station, the received data will be adjusted in software to compensate for thermocouple cold-junction reference and then displayed in a near-real-time format. The entire product, both the hardware and software, will be as modular as possible. This is to allow for expansion into other applications as well as to facilitate improvements.

# Study Organization

The research, design, implementation, and testing for this project will be organized in the manner depicted in Table 4 and Figure 6. The high-level organization of this project can be described as starting with research and concept generation, followed by design and experimentation of the various functional segments, construction, and then testing and verification. The sequence and duration of the major tasks of this project are shown in Figure 2.

As shown in Table 4, the major tasks of this project will be generating the project idea, research, creating a concept generation matrix, thermocouple/analog circuit experimentation and design, MSP430-Transceiver experimentation and design, TSA experimentation and design, RSA design, PCSA design and software development, PCB layout, assembly, testing and reconfiguration, documentation review, and demonstration. Major milestones of the project include the finalization of the project idea, completion of the system-level design and detailed design, completion of assembly, and completion of testing and verification.

Table 4: Task Breakdown

Figure 6: Project Timeline

# References

Table 5 lists the various resources that have been referenced during the development of this product.

| Reference | Description | Reference capacity | Link to resource |
| --- | --- | --- | --- |
| Thermocouple reference chart | Chart that differentiates between thermocouple type, temperature range, composition, color code, voltage range, etc. | Specifications and standards | http://www.omega.com/techref/colorcodes.html |
| Texas Instruments | Integrated Circuit (IC) manufacturer | Data sheets, product features, and pricing information for various ICs | http://www.ti.com/ |
| Analog Devices | Integrated Circuit (IC) manufacturer | Data sheets, product features, and pricing information for various amplifiers, voltage regulators, and DC-to-DC converters | http://www.analog.com |
| Spark Fun Electronics | Electronics distributor and development board manufacturer | Data sheets, product features, and pricing information for various transceivers and microcontrollers | www.sparkfun.com/ |
| Dr. Karl Gugel | Professor and owner of Digital Control Lab | Technical direction | gugel@ecel.ufl.edu |
| Tsang Wei Huang | Graduate student and Teaching Assistant | Technical support | twhuang@ufl.edu |
| Grzegorz Cieslewski | Graduate student, Teaching Assistant, Research Assistant | Technical support | grzegorz@ufl.edu |

Table 5: Project references

# Materials and Resources

Table 6 shows a general list of anticipated major components for this project, including the subassemblies in which they will reside. Resources needed for this project include a multi-channel thermocouple simulator, PCB design software, and access to relevant industry testing environments.

| Functional Assemblies | Subassemblies | Components |
| --- | --- | --- |
| Transmit-Side Assembly (TSA) | Power management | DC/DC boosters and/or regulators |
|  | Thermocouple/analog circuit | Thermocouples |
|  |  | Analog multiplexers |
|  |  | Variable-gain amplifier |
|  | Data processing | A/D converter |
|  |  | Microcontroller |
|  | Data transmission | Wireless transceiver |
| Receive-Side Assembly (RSA) | Power management | Voltage regulator |
|  | Data receive | Wireless Transceiver |
|  | Data processing | Microcontroller |
|  | Serial communication | RS232 line driver |
|  |  | RS485 line driver |
| PC-Side Assembly (PCSA) | Power management | Voltage regulator |
|  | Data processing | RS232 line receiver |
|  |  | RS485 line receiver |
|  |  | Microcontroller |
|  |  | Serial to USB interface |

Table 6: Major project resources