Date: June 15, 2006

Student Name: John Miller III

TAs : Adam Barnett,

William Otto Goethals

Instructors: A. A Arroyo

E. M. Schwartz

University of Florida

Department of Electrical and Computer Engineering

EEL 5666 Intelligent Machines Design Laboratory

## Weekly Report 5 (15 June, 2006)

## This past week I have gotten the LCD to work and display any information I wish. I had to rewire the LED’s for the backlight of the LCD. I cannot believe that they had it wrong! Anyways, I also interfaced my Sharp 31” trigger sensors to my Atmel and can control multiple outputs depending on the readings. I am currently working on an “if then” state machine that I can code for obstacle avoidance. I have also gotten the water pump to work and spray water out of my barrel. I am not impressed with the water pressure, so I am experimenting with a few nozzles, voltages, and motors. I tried running the motors through standard mosfets but that did not seem to work too well, so I ordering h-bridge motors drivers.

Commentary on the Laboratory

I have been working out of my home lab, so I have no useful comments.